## Slide 1
Chapter 1
Fundamentals of Quantitative Design and Analysis
Computer Architecture
A Quantitative Approach, Fifth Edition

## Slide 2: Computer Technology
Performance improvements:
  Improvements in semiconductor technology
    Feature size, clock speed
  Improvements in computer architectures
    Enabled by HLL compilers, UNIX
    Lead to RISC architectures
  Together have enabled:
    Lightweight computers
    Productivity-based managed/interpreted programming languages
    SaaS, Virtualization, Cloud
  Applications evolution:
    Speech, sound, images, video, “augmented/extended reality”, “big data”
Introduction

## Slide 3: Single Processor Performance
Introduction
RISC
Move to multi-processor

## Slide 4: Current Trends in Architecture
Cannot continue to leverage Instruction-Level parallelism (ILP)
  Single processor performance improvement ended in 2003
New models for performance:
  Data-level parallelism (DLP)
  Thread-level parallelism (TLP)
  Request-level parallelism (RLP)
These require explicit restructuring of the application
Introduction

## Slide 5: Classes of Computers
Personal Mobile Device (PMD)
  e.g. smart phones, tablet computers (1.8 billion sold 2010)
  Emphasis on energy efficiency and real-time
Desktop Computing
  Emphasis on price-performance (0.35 billion)
Servers
  Emphasis on availability (very costly downtime!), scalability, throughput (20 million)
Clusters / Warehouse Scale Computers
  Used for “Software as a Service (SaaS)”, PaaS, IaaS, etc.
  Emphasis on availability ($6M/hour-downtime at Amazon.com!) and price-performance (power=80% of TCO!)
  Sub-class: Supercomputers, emphasis: floating-point performance and fast internal networks, and big data analytics
Embedded Computers (19 billion in 2010)
  Emphasis: price
Classes of Computers

## Slide 6: Parallelism
Classes of parallelism in applications:
  Data-Level Parallelism (DLP)
  Task-Level Parallelism (TLP)
Classes of architectural parallelism:
  Instruction-Level Parallelism (ILP)
  Vector architectures/Graphic Processor Units (GPUs)
  Thread-Level Parallelism
  Request-Level Parallelism
Classes of Computers

## Slide 7: Flynn’s Taxonomy
Single instruction stream, single data stream (SISD)
Single instruction stream, multiple data streams (SIMD)
  Vector architectures
  Multimedia extensions
  Graphics processor units
Multiple instruction streams, single data stream (MISD)
  No commercial implementation
Multiple instruction streams, multiple data streams (MIMD)
  Tightly-coupled MIMD
  Loosely-coupled MIMD
Classes of Computers

## Slide 8: Defining Computer Architecture
“Old” view of computer architecture:
  Instruction Set Architecture (ISA) design
  i.e. decisions regarding:
    registers, memory addressing, addressing modes, instruction operands, available operations, control flow instructions, instruction encoding
“Real” computer architecture:
  Specific requirements of the target machine
  Design to maximize performance within constraints: cost, power, and availability
  Includes ISA, microarchitecture, hardware
Defining Computer Architecture

## Slide 9: Trends in Technology
Integrated circuit technology
  Transistor density: 35%/year
  Die size: 10-20%/year
  Integration overall: 40-55%/year
DRAM capacity: 25-40%/year (slowing)
Flash capacity: 50-60%/year
  15-20X cheaper/bit than DRAM
Magnetic disk technology: 40%/year
  15-25X cheaper/bit then Flash
  300-500X cheaper/bit than DRAM
Trends in Technology

## Slide 10: Bandwidth and Latency
Bandwidth or throughput
  Total work done in a given time
  10,000-25,000X improvement for processors over the 1st milestone
  300-1200X improvement for memory and disks over the 1st milestone
Latency or response time
  Time between start and completion of an event
  30-80X improvement for processors over the 1st milestone
  6-8X improvement for memory and disks over the 1st milestone
Trends in Technology

## Slide 11: Bandwidth and Latency
Log-log plot of bandwidth and latency milestones
Trends in Technology

## Slide 12: Transistors and Wires
Feature size
  Minimum size of transistor or wire in x or y dimension
  10 microns in 1971 to .032 microns in 2011
  Transistor performance scales linearly
    Wire delay does not improve with feature size!
  Integration density scales quadratically
  Linear performance and quadratic density growth present a challenge and opportunity, creating the need for computer architect!
Trends in Technology

## Slide 13: Power and Energy
Problem: Get power in, get power out
Thermal Design Power (TDP)
  Characterizes sustained power consumption
  Used as target for power supply and cooling system
  Lower than peak power, higher than average power consumption
Clock rate can be reduced dynamically to limit power consumption
Energy per task is often a better measurement
Trends in Power and Energy

## Slide 14: Dynamic Energy and Power
Dynamic energy
  Transistor switch from 0 -> 1 or 1 -> 0
  ½ x Capacitive load x Voltage2
Dynamic power
  ½ x Capacitive load x Voltage2 x Frequency switched
Reducing clock rate reduces power, not energy
Trends in Power and Energy

## Slide 15: Power
Intel 80386 consumed ~ 2 W
3.3 GHz Intel Core i7 consumes 130 W
Heat must be dissipated from 1.5 x 1.5 cm chip
This is the limit of what can be cooled by air
Trends in Power and Energy

## Slide 16: Reducing Power
Techniques for reducing power:
  Do nothing well
  Dynamic Voltage-Frequency Scaling
  Low power state for DRAM, disks
  Overclocking, turning off cores
Trends in Power and Energy

## Slide 17: Static Power
Static power consumption
  Currentstatic x Voltage
  Scales with number of transistors
  To reduce: power gating
  Race-to-halt
The new primary evaluation for design innovation
  Tasks per joule
  Performance per watt
Trends in Power and Energy

## Slide 18: Trends in Cost
Cost driven down by learning curve
  Yield
DRAM: price closely tracks cost
Microprocessors: price depends on volume
  10% less for each doubling of volume
Trends in Cost

## Slide 19: Integrated Circuit Cost
Integrated circuit
Bose-Einstein formula:
Defects per unit area = 0.016-0.057 defects per square cm (2010)
N = process-complexity factor = 11.5-15.5 (40 nm, 2010)
The manufacturing process dictates the wafer cost, wafer yield and defects per unit area
The architect’s design affects the die area, which in turn affects the defects and cost per die
Trends in Cost

## Slide 20: Dependability
Systems alternate between two states of service with respect to SLA/SLO:
  Service accomplishment, where service is delivered as specified by SLA
  Service interruption, where the delivered service is different from the SLA
Module reliability: “failure(F)=transition from 1 to 2” and “repair(R)=transition from 2 to 1”
  Mean time to failure (MTTF)
  Mean time to repair (MTTR)
  Mean time between failures (MTBF) = MTTF + MTTR
  Availability = MTTF / MTBF
Dependability

## Slide 21: Measuring Performance
Typical performance metrics:
  Response time
  Throughput
Speedup of X relative to Y
  Execution timeY / Execution timeX
Execution time
  Wall clock time: includes all system overheads
  CPU time: only computation time
Benchmarks
  Kernels (e.g. matrix multiply)
  Toy programs (e.g. sorting)
  Synthetic benchmarks (e.g. Dhrystone)
  Benchmark suites (e.g. SPEC06fp, TPC-C)
Measuring Performance

## Slide 22: Principles of Computer Design
Take Advantage of Parallelism
  e.g. multiple processors, disks, memory banks, pipelining, multiple functional units
Principle of Locality
  Reuse of data and instructions
Focus on the Common Case
  Amdahl’s Law
Principles

## Slide 23: Principles of Computer Design
The Processor Performance Equation
Principles

## Slide 24: Principles of Computer Design
Principles
Different instruction types having different CPIs

## Slide 25: Instruction Set Architecture (ISA)
Serves as an interface between software and hardware.
Provides a mechanism by which the software tells the hardware what should be done.
instruction set
High level language code : C, C++, Java, Fortran,
hardware
Assembly language code: architecture specific statements
Machine language code: architecture specific bit patterns
software
compiler
assembler

## Slide 26: Instruction Set Design Issues
Instruction set design issues include:
  Where are operands stored?
    registers, memory, stack, accumulator
  How many explicit operands are there?
    0, 1, 2, or 3
  How is the operand location specified?
    register, immediate, indirect, . . .
  What type & size of operands are supported?
    byte, int, float, double, string, vector. . .
  What operations are supported?
    add, sub, mul, move, compare . . .

## Slide 27: Classifying ISAs
Accumulator (before 1960, e.g. 68HC11):
1-address add A acc ¬ acc + mem[A]
Stack (1960s to 1970s):
0-address add tos ¬ tos + next
Memory-Memory (1970s to 1980s):
2-address add A, B mem[A] ¬ mem[A] + mem[B]
3-address add A, B, C mem[A] ¬ mem[B] + mem[C]
Register-Memory (1970s to present, e.g. 80x86):
2-address add R1, A R1 ¬ R1 + mem[A]
load R1, A R1 ¬ mem[A]
Register-Register (Load/Store, RISC) (1960s to present, e.g. MIPS):
3-address add R1, R2, R3 R1 ¬ R2 + R3
load R1, R2 R1 ¬ mem[R2]
store R1, R2 mem[R1] ¬ R2

## Slide 28: Operand Locations in Four ISA Classes
GPR

## Slide 29: Code Sequence C = A + B for Four Instruction Sets
Stack | Accumulator | Register (register-memory) | Register (load-store)
Push A Push B Add Pop C | Load A Add B Store C | Load R1, A Add R1, B Store C, R1 | Load R1,A Load R2, B Add R3, R1, R2 Store C, R3
memory
memory
acc = acc + mem[C]
R1 = R1 + mem[C]
R3 = R1 + R2

## Slide 30: Types of Addressing Modes (VAX)
Addressing Mode Example Action
1. Register direct Add R4, R3 R4 <- R4 + R3
2. Immediate Add R4, #3 R4 <- R4 + 3
3. Displacement Add R4, 100(R1) R4 <- R4 + M[100 + R1]
4. Register indirect Add R4, (R1) R4 <- R4 + M[R1]
5. Indexed Add R4, (R1 + R2) R4 <- R4 + M[R1 + R2]
6. Direct Add R4, (1000) R4 <- R4 + M[1000]
7. Memory Indirect Add R4, @(R3) R4 <- R4 + M[M[R3]]
8. Autoincrement Add R4, (R2)+ R4 <- R4 + M[R2]
R2 <- R2 + d
9. Autodecrement Add R4, (R2)- R4 <- R4 + M[R2]
R2 <- R2 - d
10. Scaled Add R4, 100(R2)[R3] R4 <- R4 +
M[100 + R2 + R3*d]
Studies by [Clark and Emer] indicate that modes 1-4 account for 93% of all operands on the VAX.

## Slide 31: Types of Operations
Arithmetic and Logic: AND, ADD
Data Transfer: MOVE, LOAD, STORE
Control BRANCH, JUMP, CALL
System OS CALL, VM
Floating Point ADDF, MULF, DIVF
Decimal ADDD, CONVERT
String MOVE, COMPARE
Graphics (DE)COMPRESS

## Slide 32: MIPS Instructions
All instructions exactly 32 bits wide
Different formats for different purposes
Similarities in formats ease implementation
op
rs
rt
offset
6 bits
5 bits
5 bits
16 bits
op
rs
rt
rd
funct
shamt
6 bits
5 bits
5 bits
5 bits
5 bits
6 bits
R-Format
I-Format
op
address
6 bits
26 bits
J-Format
31
0
31
0
31
0

## Slide 33: MIPS Instruction Types
Arithmetic & Logical - manipulate data in registers add $s1, $s2, $s3 $s1 = $s2 + $s3 or $s3, $s4, $s5 $s3 = $s4 OR $s5
Data Transfer - move register data to/from memory  load & store lw $s1, 100($s2) $s1 = Memory[$s2 + 100] sw $s1, 100($s2) Memory[$s2 + 100] = $s1
Branch - alter program flow beq $s1, $s2, 25 if ($s1==$s1) PC = PC + 4 + 4*25
else PC = PC + 4

## Slide 34: MIPS Arithmetic & Logical Instructions
Instruction usage (assembly) add dest, src1, src2 dest=src1 + src2 sub dest, src1, src2 dest=src1 - src2 and dest, src1, src2 dest=src1 AND src2
Instruction characteristics
  Always 3 operands: destination + 2 sources
  Operand order is fixed
  Operands are always general purpose registers
Design Principles:
  Design Principle 1: Simplicity favors regularity
  Design Principle 2: Smaller is faster

## Slide 35: Arithmetic & Logical Instructions - Binary Representation
Used for arithmetic, logical, shift instructions
  op: Basic operation of the instruction (opcode)
  rs: first register source operand
  rt: second register source operand
  rd: register destination operand
  shamt: shift amount (more about this later)
  funct: function - specific type of operation
Also called “R-Format” or “R-Type” Instructions
op
rs
rt
rd
funct
shamt
6 bits
5 bits
5 bits
5 bits
5 bits
6 bits
0
31

## Slide 36: Arithmetic & Logical Instructions - Binary Representation Example
op
rs
rt
rd
funct
shamt
6 bits
5 bits
5 bits
5 bits
5 bits
6 bits
Decimal
Binary
Machine language for add $8, $17, $18
See reference card for op, funct values
000000
0
10001
17
10010
18
01000
8
00000
0
100000
32
0
31

## Slide 37: MIPS Data Transfer Instructions
Transfer data between registers and memory
Instruction format (assembly) lw $dest, offset($addr) load word sw $src, offset($addr) store word
Uses:
  Accessing a variable in main memory
  Accessing an array element