## Slide 1: SARP: Spatial Agnostic Radio Fingerprinting with Pseudo-Labeling
Fahmida Afrin⃰, Haipeng Li⸶, Boyang Wang⸶, and Nirnimesh Ghose ⃰
⃰ School of Computing, University of Nebraska – Lincoln
⸶Department of Electrical and Computer Engineering, University of Cincinnati
IEEE Consumer Communications & Networking Conference
January 10–13, 2025

## Slide 2: Introduction
No two devices share an identical fingerprint.
Uses:
Device Identification
Device Authentication
RF fingerprinting

## Slide 3: Radio Frequency (RF) Fingerprinting
Uniqueness Causes:
Hardware impairment caused by manufacturing process variation.
Serves as discriminative features
Examples: Phase Noise, Nonlinear Distortion, IQ imbalance, DC offset, Non-linear power amplifier gain, among others.

## Slide 4: Motivation
Poor performance of traditional deep-learning models in radio fingerprinting under spatial variations.
Mitigate the loss of critical interdependencies caused by separating real and imaginary components in real-valued CNNs.
Bridge the gap in applying Complex-Valued Neural Networks (CVNNs) to real-world RF signals with spatial variations.
Reduce dependency on labeled data from new locations.

## Slide 5: Objectives
Develop a CVNN-based method with pseudo-labeling for spatially robust fingerprinting.
Fine-tune models with unlabeled data while retaining I/Q component correlations.
Validate real-world datasets and optimize activation functions for accuracy.

## Slide 6: System Model
Setup:
Multiple transmitters, one receiver.
Training Phase:
Receiver collects RF signals
Server trains a classifier.
Authentication Phase:
Classifier identifies transmitters from new RF signals.

## Slide 7: Threat Model
Training Phase:
  Trusted participants.
Authentication Phase:
  Trained Attackers: e.g., Tx3 impersonating Tx1/Tx2.
  Untrained Attackers: e.g., A1/A2 impersonating Tx1/Tx2/Tx3

## Slide 8: SARP: Proposed Method
Combine Complex-Valued Neural Networks (CVNNs) and pseudo-labeling to address spatial variations.

## Slide 9: Architecture & Settings
Hardware: Tesla V100 GPU, cuDNN 8.6.0.
Model: CVNN, 100 epochs, 0.1 learning rate, early stopping (patience 10).
Dataset: 10,000 I/Q traces, 72% train, 8% val, 20% test.

## Slide 10: Experimental Setup
Transmitters: 3 USRP 2922 and 7 USRP B200-mini-i.
Receiver: 1 USRP B205-mini-i device.
Modulation: Wi-Fi transmissions using BPSK ½
Locations: I/Q_Loc1–I/Q_Loc4, devices stationary, 3 ft apart.
Parameters:
  Center frequency: 2.45 GHz.
  Bandwidth: 2.5 MHz
  Sampling rate: 5 MHz
Sessions: 3 sessions/location, 30 sec each, 30-sec gaps.

## Slide 11: Experiment A: Baseline Performance of CVNN
Test from the same location, Higher accuracy, better distinction.
Test from different locations, Lower accuracy, poor distinction.
Activation Functions: CReLU, Complex Cardioid, Cart Leaky ReLU.
(a) Train: I/Q_Loc1, test: I/Q_Loc2
(a) Train: I/Q_Loc3, test: I/Q_Loc4

## Slide 12: Experiment B: CVNN with Pseudo-Labeling
Accuracy improved to 62.8% with pseudo-labeling
Higher N boosted accuracy.
θ = 0.7 gave best accuracy
(a) Train: I/Q_Loc1, test: I/Q_Loc2
(a) Train: I/Q_Loc3, test: I/Q_Loc4

## Slide 13: Experiment C: Timing information
Training: 7,200 I/Q traces (1.4 ms).
Fine-Tuning: 200–800 I/Q traces (20–160μs).
Finding: Pseudo-labeling improved cross-location performance.

## Slide 14: Conclusion and Future Work
Improved model accuracy by using I/Q data as a single input to a CVNN.
Addressed domain shifts with pseudo-labeling for varying wireless environments.
Demonstrated CVNN outperforms CNN in radio fingerprinting.
Thank you for listening!!!
Questions???