## Slide 1: CSCE 230, Fall 2013 Appendix A: Logic Circuits, part 1
Acknowledgement: Overheads adapted from those provided by the authors of the textbook
Logic Circuits
Mehmet Can Vuran, Instructor
University of Nebraska-Lincoln

## Slide 2: Logic Design
Notes: 2

## Slide 3: Logic Design
Notes: 3

## Slide 4: Logic Implementation Choices
Programmable
  Software
    Typically, use single-board microcontrollers to implement the logic by a program
  Programmable logic devices (PLDs) and field programmable gate arrays (FPGAs)
    Devices in which the logic elements and the interconnect (wiring) can be modified by programming.
    Ideal for rapid prototyping and low-volume applications.
  ROMs
Custom Designs
  How Intel designs microprocessors
  Cost-effective only for high-volume parts
Notes: 4

## Slide 5: Logic circuits
Operate on binary variables that assume one of two distinct values, usually called 0 and 1
Implement functions of logic variables
Circuits have inputs and outputs
Circuits are implemented using electronic logic gates

## Slide 6: Basic Gates
AND
OR
NOT
B
A
B
A
C
B
A
C

## Slide 7: Truth Tables
A | B | C
0 | 0 | 
0 | 1 | 
1 | 0 | 
1 | 1 | 
B
A
B
A
C
B
A
C
AND

## Slide 8: Basic Gates and Truth Tables
A | B | C
0 | 0 | 0
0 | 1 | 0
1 | 0 | 0
1 | 1 | 1
B
A
B
A
C
B
A
C
AND

## Slide 9: Basic Gates and Truth Tables
A | B | C
0 | 0 | 0
0 | 1 | 0
1 | 0 | 0
1 | 1 | 1
B
A
B
A
C
B
A
C
A | B | C
0 | 0 | 
0 | 1 | 
1 | 0 | 
1 | 1 | 
AND
OR

## Slide 10: Basic Gates and Truth Tables
A | B | C
0 | 0 | 0
0 | 1 | 0
1 | 0 | 0
1 | 1 | 1
B
A
B
A
C
B
A
C
A | B | C
0 | 0 | 0
0 | 1 | 1
1 | 0 | 1
1 | 1 | 1
AND
OR

## Slide 11: Basic Gates and Truth Tables
NOT
A | B | C
0 | 0 | 0
0 | 1 | 0
1 | 0 | 0
1 | 1 | 1
B
A
B
A
C
B
A
C
A | B | C
0 | 0 | 0
0 | 1 | 1
1 | 0 | 1
1 | 1 | 1
A | B
0 | 
1 | 
AND
OR

## Slide 12: Basic Gates and Truth Tables
NOT
A | B | C
0 | 0 | 0
0 | 1 | 0
1 | 0 | 0
1 | 1 | 1
B
A
B
A
C
B
A
C
A | B | C
0 | 0 | 0
0 | 1 | 1
1 | 0 | 1
1 | 1 | 1
A | B
0 | 1
1 | 0
AND
OR

## Slide 13: Exclusive-Or
A | B | XOR
0 | 0 | 
0 | 1 | 
1 | 0 | 
1 | 1 | 
XOR

## Slide 14: Exclusive-Or
A | B | XOR
0 | 0 | 0
0 | 1 | 1
1 | 0 | 1
1 | 1 | 0
XOR

## Slide 15
Light switch example

## Slide 16: Standard logic gate symbols

## Slide 17: Why? How?

## Slide 18: Logic circuits
Operate on binary variables that assume one of two distinct values, usually called 0 and 1
Why?
Let’s back up…

## Slide 19: Let’s Back up…

## Slide 20: Transistors

## Slide 21: Basic Building Block for all Logic Gates
A | B | NAND
0 | 0 | 1
0 | 1 | 1
1 | 0 | 1
1 | 1 | 0
Not AND  NAND

## Slide 22: Basic Building Block for all Logic Gates - NAND
A | B | NAND
0 | 0 | 1
0 | 1 | 1
1 | 0 | 1
1 | 1 | 0
NAND

## Slide 23: NOT from NAND
NOT
A | B
0 | 1
1 | 0

## Slide 24: AND from NANDs
AND
A | B | C
0 | 0 | 0
0 | 1 | 0
1 | 0 | 0
1 | 1 | 1

## Slide 25: OR from NAND
OR
A | B | C
0 | 0 | 0
0 | 1 | 1
1 | 0 | 1
1 | 1 | 1

## Slide 26: OR from NAND
OR
A | B | C
0 | 0 | 0
0 | 1 | 1
1 | 0 | 1
1 | 1 | 1

## Slide 27: XOR from NAND
XOR
A | B | C
0 | 0 | 0
0 | 1 | 1
1 | 0 | 1
1 | 1 | 0

## Slide 28: NOR from NAND
NOR
A | B | C
0 | 0 | 1
0 | 1 | 0
1 | 0 | 0
1 | 1 | 0

## Slide 29: XNOR from NAND
XNOR
A | B | C
0 | 0 | 1
0 | 1 | 0
1 | 0 | 0
1 | 1 | 1

## Slide 30: Implementation of the XOR function using AND, OR, and NOT gates
A | B | XOR
0 | 0 | 0
0 | 1 | 1
1 | 0 | 1
1 | 1 | 0
XOR

## Slide 31: Implementation of the XOR function using AND, OR, and NOT gates

## Slide 32: Synthesis of logic functions
Synthesis is the process of designing and implementing a logic circuit defined by its functional specification.
The expression for f in the previous circuit is said to be in a sum-of-products form
  OR and AND operations are sometimes called the sum and product functions.

## Slide 33: Implementation of a logic function

## Slide 34: Implementation of a logic function

## Slide 35: Implementation of a logic function

## Slide 36: Implementation of a logic function

## Slide 37: Proving equivalence of expressions

## Slide 38: Rules of binary logic

## Slide 39: Example
Show a logic equation for the three functions shown in the following truth table:

## Slide 40: Minimization of logic expressions
As illustrated in the previous example, a logic function can be implemented with circuits of different complexities.
It is useful to minimize a logic expression to reduce the cost of the synthesized circuit.

## Slide 41: Karnaugh Maps

## Slide 42: Three-variable Karnaugh maps

## Slide 43
Four-variable
Karnaugh maps

## Slide 44
Using don’t cares

## Slide 45: NAND and NOR gates

## Slide 46: Equivalence of NAND-NAND and AND-OR networks

## Slide 47: Cascading of gates

## Slide 48: Section A.5 Practical Implementation of Logic Gates Read the Chapter in detail and study the following slides, we will skip most of them in class

## Slide 49: Representation of logic values by voltage levels

## Slide 50: NMOS and PMOS transistors
NMOS Transistor

## Slide 51: An inverter circuit

## Slide 52: A transistor circuit implementation of a NOR gate

## Slide 53: A transistor circuit implementation of a NAND gate

## Slide 54: NMOS and PMOS transistors
PMOS Transistor

## Slide 55: CMOS realization of a NOT gate

## Slide 56: Structure of a CMOS circuit

## Slide 57: CMOS realization of a NAND gate

## Slide 58: CMOS realization of a NOR gate

## Slide 59: CMOS realization of an AND gate

## Slide 60: The voltage transfer characteristic for the CMOS inverter

## Slide 61: Definition of propagation delay and transition time

## Slide 62: Cascading Logic Gates
Cannot directly connect logic gates
May damage the circuits in certain input combinations
May not need ALL the gates together
If a gate is not SELECTED, it should not provide 1 or 0
Need a third output – Z (high impedance)

## Slide 63: Tri-state buffer

## Slide 64: Upcoming…
HW 3 – Chapter 3
  Assign Friday, Sept. 27th
  Due Wednesday, Oct. 9th
Test 1 – Chapters 1-2
  Monday, Oct. 7th (50 min)
Quiz 3 – Chapter 3
  Friday, Oct. 11th (15 min)