## Slide 1: CSCE 230, Fall 2013 Chapter 1, part 1 Basic Structure of Computers
Mehmet Can Vuran, Instructor
University of Nebraska-Lincoln
Acknowledgement: Overheads adapted from those provided by the authors of the textbook

## Slide 2: Chapter Outline
computer types, structure, and operation
instructions and programs
numbers, arithmetic operations, and characters
performance issues

## Slide 3: What is a computer?
Components:
  input (mouse, keyboard)
  output (display, printer)
  memory (disk drives, DRAM, SRAM, CD)
  network
  processor

## Slide 4: What is a computer?
Components:
  input (mouse, keyboard)
  output (display, printer)
  memory (disk drives, DRAM, SRAM, CD)
  network
  processor

## Slide 5: Inside the Processor (CPU)
Datapath: performs operations on data
Control: sequences datapath, memory, ...
Cache memory
  Small fast SRAM memory for immediate access to data

## Slide 6: Inside the Processor
AMD Barcelona: 4 processor cores

## Slide 7: Processor
  implemented using millions of transistors
  Impossible to understand by looking at each transistor
  We need...

## Slide 8: Abstractions
Abstraction helps us deal with complexity
  Hide lower-level detail
Instruction set architecture (ISA)
  The hardware/software interface
Application binary interface
  The ISA plus system software interface
Implementation
  The details underlying and interface

## Slide 9: Computer Architecture
CPU
mem
input
output
analog
analog
computer

## Slide 10: CPU + memory
memory
CPU
PC
address
data
IR
ADD r5,r1,r3
200
200
ADD r5,r1,r3

## Slide 11: Memory Structure
Processor
Cache
Primary
Memory
Secondary Memory

## Slide 12: Functional units
Secondary memory
Magnetic disks, optical disks, flash memory devices
Used to store program and data files
Stored data organized hierarchically, e.g. sectors, tracks, cylinders, etc. for a magnetic disk.

## Slide 13: Functional units
Primary memory (also called Main memory)
Hierarchical: Banks, blocks, words, bytes, bit cells.
Semiconductor bit cells, organized into words of typically 32 bits
A 32-bit word contains four 8-bit bytes
Programs and their data must be in this memory to be executed
Memory cells have associated addresses
Can read or write a word or a block at a time, given its address.

## Slide 14: Instructions and Programs
An instruction specifies an operation and the locations of its data operands
A 32-bit word typically holds one encoded instruction
A program in static form consists of sequence of instructions; its dynamic form corresponds to the sequence of instructions executed during a particular run.
Both a program and its data are stored in the main memory

## Slide 15: Program and Data in Memory
.
.
.
.
.
.
A
B
C
Data
Program
Load R1, B
Load R2, C
Add R3, R1, R2
Store R3, A
i
i+4
i+8
i+12
Addresses
<value of A>
<value of B>
<value of C>

## Slide 16: Functional units
Cache memory
An adjunct to the main memory, fabricated on the processor chip
Much smaller and faster than the main memory
Holds sections of the program and data currently being executed

## Slide 17: Functional units
Processor
logic circuits for performing arithmetic and logic operations on word-size data operands
timing and control circuits for fetching program instructions and data from memory, one after another
registers (typically 16 or 32), each of which hold one word of operand data

## Slide 19: Processor components
The program counter (PC) register holds the memory address of the current instruction
The instruction register (IR) holds the current instruction
General purpose registers hold data and addresses
Control circuits and the arithmetic and logic unit (ALU) fetch and execute instructions

## Slide 21: Instruction types
Three basic instruction types:
Load - Read a data operand from memory or an input device into the processor
Store - Write a data operand from a processor register to memory or an output device
Operate - Perform an arithmetic, logic operation on data operands in processor registers

## Slide 22: Program and Data in Memory
.
.
.
.
.
.
A
B
C
Data
Program
Load R1, B
Load R2, C
Add R3, R1, R2
Store R3, A
i
i+4
i+8
i+12
Addresses
<value of A>
<value of B>
<value of C>

## Slide 23: Example program
A, B, and C, are labels representing memory word addresses; Ri are processor registers
A program for the calculation A = B + C is: Load R1, B Load R2, C Add R3, R1, R2 Store R3, C

## Slide 24: Fetching and executing instructions
Example: Load R2, LOC The processor control circuits do the following:
Send address in PC to memory; issue Read
Load instruction from memory into IR
Increment PC to point to next instruction
Send address LOC to memory; issue Read
Load word from memory into register R2

## Slide 25: Two Levels of Interpretation
HLL
Machine
Language
Hardware
A=B+C
Load R1, B Load R2, C Add R3, R1, R2 Store R3, C

## Slide 26: Handling I/O devices
An application program can:
Read data (such as a keyboard character) from an input device
Write data (such as letter character) to an output display screen
Sense the readiness of an input or output (I/O) device to perform a transfer

## Slide 27: Interrupts
A device ( such as an alarm indicator) can raise an interrupt signal to cause a service program to be executed
The interrupt signal causes the processor to
suspend the current program and execute an
interrupt-service program