## Slide 1: CSCE 230, Fall 2013 Chapter 1, part 2 Number Systems
Mehmet Can Vuran, Instructor
University of Nebraska-Lincoln
Acknowledgement: Overheads adapted from those provided by the authors of the textbook

## Slide 2: Decimal Number Representation & Arithmetic

## Slide 3: Overview
We will illustrate the basic concepts of number representation using the familiar decimal base or radix.
Concepts generalize to any other base.
Consider three categories of numbers
  Unsigned Integers
  Signed Integers
  Floating-point numbers (“Reals”)

## Slide 4: Unsigned Integers
Useful for representing addresses, IDs, etc. In computers, useful for representing memory addresses.
Positional notation
  Radix or base, e.g.
    3810 = 3*101 + 8*100
    1001102 = 1*25+0*24+0*23+1*22+1*21+0*20 = 32+4+2 = 4210
When number of digits of representation is bounded, we use modulo arithmetic. E.g.
  With 2 decimal digits: 99+1 = 0 (modulo 100)

## Slide 5: Exercises
Express 4210 in ternary (base 3) and hexadecimal (base 16) representations.
Express: A68C16 == 0xA68C as a decimal number.
Express 20123 as a decimal number.
Express 100111000112 as the equivalent hexadecimal number.
(you can do these conversions using online tools but I would like you to learn algorithmic ways to do them. These will be explained in recitation; follow up with sources on the Internet).

## Slide 6: Signed Integers: Unbounded Range
First consider unbounded number of digits available for representation. Also decimal representation
Two common representations:
  Sign-magnitude, e.g. +267, -37, ..
  10’s complement

## Slide 7: 9’s Complement
Define 9’s complement of integer x as:
    …999…999 – x
    E.g. 9’s complement of ...00675 = …99324
  and represent negative integers by their 9’s complement. Positives in the usual way.
Can do away with the + or - sign: leading 0’s represent positives and leading 9’s represent negatives.

## Slide 8: 9’s complement arithmetic
Perform 532 – 20 in 9’s complement
Equivalent to 532 + (-20)
In 9’s complement, we have
    …00532
    + …99979
    …00511 (hence 1 to the result if there is carry out of the sign bits)
What if we computed 20 – 532 in 9’s complement?
    …00020
    + …99467
    …99487 = -512 (hence when there is no carry, the result is correct)

## Slide 9: 10’s Complement
Define 10’s complement of integer x as:
    …000 – x (ignore borrow)
    E.g. 10’s complement of ...00532:
    …00000
    - …00532
    99468
Represent positives same as unsigned, negatives by the 10’s complement of their magnitude.
No explicit + or – sign needed. Leading 9’s represent negatives and leading 0’s positives.

## Slide 10: 10’s Complement Arithmetic
Perform 20 + (-532) in 10’s complement
    00020
  + 99468
  99488 (verify that this is equal to -512 by negating it, i.e. subtracting from …00000 and ignoring the borrow.

## Slide 11: Limited Range
When signed integers can only be represented by a limited number of digits, only a limited range of numbers can be represented.
Numbers falling outside this range will cause overflow or underflow.
There are simple ways of detecting these situations.

## Slide 12: Limited Range: 9’s Complement
Assume only two decimal digits available for representation.
What is the range of representable numbers?
  Positives: 000 to 099 (where the leading 0 means the number is positive)
  Negatives: 900 to 999 or -9910 to -0010
Note: Two representations for 0. Range is [-99, +100].

## Slide 13: Overflow in 9’s complement
Perform 6710 + 4510 in 9’s complement:
067
+ 045
112
(The overflow is indicated by the incorrect sign digit –should be 0 instead of 1)
Perform (-6710)+(-4510) in 9’s complement:
932
+ 954
886+1 (end around carry) = 867
(Again, the overflow is indicate by the incorrect sign digit – should be 9 instead of 8).

## Slide 14: Limited Range: 10’s Complement
Assume only two decimal digits available for representation of number (3 digits in total).
What is the range of representable numbers?
  Positives: 000 to 099 (where the leading 0 means the number is positive)
  Negatives: 900 to 999 or -10010 to -0010
The range is [-100, +99].

## Slide 15: Overflow in 10’s complement
Perform 6710 + 4510 in 10’s complement:
067
+ 045
112
(The overflow is indicated by the incorrect sign digit –should be 0 instead of 1)

## Slide 16: Binary Number Representation & Arithmetic

## Slide 17: Numbers
A 32-bit integer in positional binary notation has its bits labeled as:
B = b31 b30 . . . b1 b0
If bit bi = 1, then 2i is added into the sum that determines the value of B

## Slide 18: Unsigned Binary Numbers
Bit Position: | 3 | 2 | 1 | 0
Binary Number: | 1 | 0 | 1 | 1
Bit Value: | 8 | 4 | 2 | 1
Unsigned Value: | 1x8 | 0x4 | 1x2 | 1x1
= 8+0+2+1 =11
Positional Notation:

## Slide 19: Adding Two Unsigned Binary
Example of adding 4-bit unsigned numbers:
Binary Decimal
Number 1: 0 1 0 1 5
Number 2: 0 0 0 1 1
Carry_in/out: 0 0 1 0 0
Sum: 0 1 1 0 6

## Slide 20: Binary Addition Table
Binary addition of two numbers can be carried out by table lookup for each bit position, from right to left.
Bit 1 | Bit 2 | Bit 3 (Carry-in) | Carry-out | Sum
0 | 0 | 0 | 0 | 0
0 | 0 | 1 | 0 | 1
0 | 1 | 0 | 0 | 1
0 | 1 | 1 | 1 | 0
1 | 0 | 0 | 0 | 1
1 | 0 | 1 | 1 | 0
1 | 1 | 0 | 1 | 0
1 | 1 | 1 | 1 | 1

## Slide 21: Signed Binary Numbers and Arithmetic

## Slide 22: Signed Binary Numbers
For signed integers, the leftmost bit always
indicates the sign:
0 for positive
1 for negative
There are three ways to represent signed integers:
Sign and magnitude
1’s complement
2’s complement

## Slide 23: Sign-Magnitude Representation
Put the sign bit (0 for plus, 1 for minus) in front of the unsigned number:
Examples:
  +1110: 0 10112
  -1110: 1 10112

## Slide 24: 1’s Complement Representation
Positives same as in Sign-Magnitude. Negatives represented by 1’s complement of their magnitude.
Examples:
  +1110: 0 10112
  -1110: 1 <1’s complement of 10112>
  = 1 0100

## Slide 25: 2’s Complement Representation
Positives same as in Sign-Magnitude. Negatives represented by 2’s complement of their magnitude.
Examples:
  +1110: 0 10112
  -1110: 1 <2’s complement of 10112>
  = 1 <1’s complement of 10112+1> = 1 0100
  + 1
1 0101

## Slide 26: Negation of a Signed Number
Sign-Magnitude: Flip the sign bit
1’s Complement : Flip all the bits
2’s Complement:
  Flip all the bits, add 1, and Ignore carry from the left-most bit), or
  Subtract from 0 and ignore carry from the left-most bit.

## Slide 28: Addition in 2’s Complement
Examples of adding 4-bit numbers
0 0 0 1 +1 0 1 0 0 +4
+ 0 1 011 + +5 + 1 0 1 0 + -6
-------------- -------- ------------- ------
0 1 1 0 +6 1 1 1 0 -2

## Slide 29: C = A+B in Sign Magnitude
s(A)=
s(B)?
Y
m(C)=
m(A)+m(B)
s(C)=s(A)
N
m(A)>m(B)?
m(C)=
m(A)-m(B)
m(C)=
M(B)-m(A)
s(C)=s(A)
s(C)=s(B)
Detect Overflow

## Slide 30: C = A+B in 1’s Complement
1c(C)=
1c(A)+1c(B)
Detect Overflow
Carry?
Y
N
1c(C)=
1c(C) + 1

## Slide 31: C = A+B in 2’s Complement
2c(C)=
2c(A)+2c(B)
Detect Overflow

## Slide 32: Subtraction in 2’s Complement
Form the 2’s complement of the subtrahend and then perform addition
1 1 1 0 -2 1 1 1 0
- 1 0 1 1 - -5 + 1 011 0 01
------------ ------ --------------
+3 0 0 1 1

## Slide 33: 2’s Complement
Let’s solve…
2+3
4+(-6)
(-5)+(-2)
7+(-3)
(-3)-(-7)
2-4
6-3
(7)-(-5)
(-7)-1
2-(-3)

## Slide 34: Overflow in 2’s Complement
Two examples of overflow; that is, when the answer does not fit in the number range
0 1 1 0 +6 1 1 1 0 -2
+ 011 0 0 + +4 11 0 0 1 + -7
------------ ------ ---------- ------
1 0 1 0 +10 0 1 1 1 -9

## Slide 35: Sign extension
Extend 4-bit signed integers to 8-bit signed
integers
0 1 0 1 0 0 0 0 0 1 0 1
1 1 1 0 1 1 1 1 1 1 1 0

## Slide 36: Integers vs. Fixed-Point
Integers are a special case of fixed-point representations.
For a given a sequence of digits, say, 3,1,4,5,9 in decimal, we could fix the decimal point any where to get different fixed-point values for the same digits, e.g. 31459 3145.9, …, 3.1459, .31459, …

## Slide 37: Doing Arithmetic with Fixed Point
Assume representing unsigned decimal integers
Want to do the following sum:
  2.457 + 0.00036
  (Note the fixed-point of given numbers does not match the fixed point of representation)

## Slide 38: Doing Arithmetic with Fixed Point
Process:
  Scale the number with smaller fraction to integer
  Use the same scale to convert the other number to integer
  Add the two integers
  “Un-scale” the result
0.00036 = 36*10^-5
2.457 = 245700*10-5
Sum = (36+245700)*10^-5 = 245736*10^-5
245736*10^-5 = 2.45736

## Slide 39: Why Floating Point?
For a given number of digits, the fixed-point range can be limiting, e.g. [0, 999] for three unsigned decimal digits.
Floating-point representation allows increased range at the cost of reduced precision.

## Slide 40: Simple Illustrative Example
Fixed point: Unsigned decimals, three digits
  Range: [0, 999]
  Precision: three decimal digits or 1 in 1000.
Floating point: Partition the three decimal digits to:
  2 digits for unsigned integers (Significand)
  1 digit for decimal scale factor (Exponent)
What is the range and precision of the floating-point representation?
(In general, both the significand and the exponent are signed fixed-point numbers.)

## Slide 41: Floating Point Representation
Consider +0.00036 in the scientific notation:
  +3.6*10^-4
  Can represent this by two fixed-point numbers: <exponent, significand> = <-4, +3.6>
Representations, based on the IEEE 754 standard, used in processors.

## Slide 42: Basic Formats: IEEE 754
Read the Wikipedia article and follow the links to
Half precision, Single Precision, Double Precision, and
Quadruple Precision for more details of each.

## Slide 43: Character encoding
American Standard Code for Information Interchange (see Wikipedia article: ASCII)
uses 7-bit codes, e.g.:
    character code
    A 1 0 0 0 0 0 1
    7 0 1 1 0 1 1 1
    + 0 1 0 1 0 1 1
The Unicode industry standard used for text in most of world’s writing systems. Can be implemented by different character encodings.
  UTF-8 uses one byte for ASCII characters, same code values
  UCS-2 (now obsolete) uses 2 bytes/char but limited in range
  UTF-16 extends UCS-2, using 4 bytes for each additional character

## Slide 44: Performance
How quickly can a program be executed ?
Some factors:
Speed of electronic circuits in the processor
Access times to the cache and main memory
Design of the instruction set
Number of operations that can be done at the same time (parallelism)

## Slide 45: Parallelism
Multiple processors, called cores, can be
fabricated on a single VLSI chip
The cores can execute different parts of a program at the same time
A large number of multi-core processors with
multiple caches and memory modules
can be organized into a multiprocessor
system to execute programs at the same time

## Slide 46: Historical perspective
Up to the 1940s: mechanical devices, electromechanical relay devices
First generation computers, 1945-1955:
vacuum tube circuits, magnetic core memories

## Slide 47: Historical perspective
Second generation, 1955-1965: transistor circuitry, magnetic disk data storage
Third generation, 1965-1975: integrated circuits for processors and memory
Fourth generation, 1975-present: microprocessors on a single VLSI chip, personal computers, embedded systems, very high performance multiprocessors

## Slide 48: Upcoming…
Review Chapter 1 and problems
HW 1 – Chapter 1
  Assign Wednesday, Sept. 4th
  Due Friday, Sept. 13th
Quiz 1 – Chapter 1
  Monday, Sept. 16th
  15 min