## Slide 1: CSCE 230, Fall 2013 Chapter 2 (part 1) Introduction to Assembly Language (§2.1–2.5 and §B.1–B.6)
Mehmet Can Vuran, Instructor
University of Nebraska-Lincoln
Acknowledgement: Overheads adapted from those provided by the authors of the textbook

## Slide 2: Simplified Assembly Notation Used in Chapter 2
Assembly languages for different processors often use different mnemonics for a given operation.
To avoid the need for details of a particular assembly language at this early stage, Chapter 2 uses English words rather than processor specific mnemonics.
This would, hopefully, ease the learning of specific assembly languages described in Appendices A–D:
  Nios II (App. B) – RISC (used in 230L)
  Coldfire (App. C) – CISC
  ARM (App. D) – RISC
  Intel IA-32 (App. E) – CISC

## Slide 3: Mapping of Variables

## Slide 4: HLL to Assembly Language: Example 1
Translate D = A+B+C to assembly
Translation Process:
  In assembly, can only add two at a time, hence
      D = A+B;
      D = D+C
  Assign variables:
    For safe keeping in memory: Locations named #A, #B, #C, and #D
    Temporarily, to processor registers R1–R4 respectively.
    (Can think of each variable as having a static image in memory and dynamic image in registers.)
  Code each assignment statement in part 1) to assembly.

## Slide 5: Translation 1
      Load R1, #A
      Load R2, #B
      Add R4, R1, R2 # D = A+B
      Load R3, #C
      Add R4, R4, R3 # D = D+C
      Store R4, #D

## Slide 6: HLL to Assembly Language: Example 1 Revisited
Translate HLL Statement: D = A+B+C to assembly, minimizing the use of registers
Key Idea: Not all variables are needed concurrently in the registers for doing the computation. Can reuse registers to minimize their number.

## Slide 7: Translation 2
      Load R1, #A
      Load R2, #B
      Add R2, R1, R2
      Load R1, #C
      Add R2, R1, R2
      Store R2, #D
Note that both R1 and R2 are reused to represent different
variables during the computation.
A good compiler tries to minimize register usage.

## Slide 8: Assembly Language Basics

## Slide 9: Instruction Characteristics
Number of operands: One, two, or three
Type: Arithmetic, Logical, Data Transfer, Control Transfer
Instruction Length: Fixed or variable – we’ll consider fixed
Addressing Modes: How operands are found

## Slide 10: Special Register R0
In many RISC architectures (including Nios II), register R0 is defined to be a read-only, constant register with value 0.
R0 = 0
Can use to implement new instructions with existing ones, e.g.
  Add R1, R0, R2 == Move R1, R2

## Slide 11: Pseudoinstructions
In the previous examples, Move is not really implemented on the processor but the assembler can translate it into a real instruction.
In general, a pseudoinstruction can be thought of as a macro translated by the assembler into one or more ISA instructions.
One of the ways, the assembly language can be made to appear richer than the ISA of the processor.

## Slide 12: Addressing Modes
      Load R1, #A
      #A  ?

## Slide 13: Addressing Modes

## Slide 14: Addressing Modes: Indirection and Pointers
Register, absolute, and immediate modes directly provide the operand or address
Other modes provide information from which the effective address of operand is derived
For program that steps through an array, can use register as pointer to next number and use the Indirect mode to access array elements:
Load R2, (R5)

## Slide 16: Addressing Modes: Indexing
Consider index mode in: Load R2, X(R5)
Effective address is given by [R5]  X
For example, assume operand address is 1020, 5 words (20 bytes) from start of array at 1000
Can put start address in R5 and use X20
Alternatively, put offset in R5 and use X1000
Base with index mode: Load Rk, X(Ri, Rj)
Effective address is given by [Ri]  [Rj]  X

## Slide 17
R5

## Slide 18
R5

## Slide 19: For Loop Semantics
Example:
  for i=0, i<N, i=i+1
  {Body of Loop}
Semantics of the three parts:
  The first part, i=0, done once, before the loop is entered
  The second part, the condition, i<N, is evaluated.
  If true, the body of the loop is executed. Then the third part, the re-initialization step i=i+1 is done and the condition is reevaluated.
  The loop terminates when the condition becomes false.

## Slide 20: For Loop Implementation
Intermediate Code
Register Map
i | N
R1 | R2
Move R1, #0
Loop: Branch_if_(i>=N) Exit
{Body of Loop}
Add R1, R1, #1
Branch Loop
Exit: …
Assembly Code
  for i=0, i<N, i=i+1
  {Body of Loop}
i=0;
Loop: if(!(i<N)) goto Exit
{Body of Loop}
i = i+1
goto Loop
Exit: …

## Slide 21: For Practice
Try implementing the following program control constructs:
  If (condition) then {…} else {…}
  While (condition) {Body of Loop}
  Do {Body of Loop} until (condition)

## Slide 22: Stepping through an Array: Solution 1 – Explicit Indexing
Example
  for i=0, i<N {A[i] = A[i]+1}
Maintain the base A[0] and offset of A[i] from A[0] in two separate registers.
Register Map:
i | N | A[i] | #A=Address A[0] | Offset A[i]
R1 | R2 | R3 | R4 | R5

## Slide 23: Stepping through an Array: Solution 1 –Index Arithmetic (Contd.)
  Initialization: R5 = 0; R4 = Address of (A[0])
  Code: Move R5, #0; Load R4, #A
Body of Loop:
  Code:
      Load R3, (R4,R5) # R3 = A[i]
      Add R3, R3, #1
      Store R3, (R4,R5) # A[i] = A[i]+1
      Add R5, R5, 4 # Update offset for the next
i | N | A[i] | Address A[0] | Offset A[i]
R1 | R2 | R3 | R4 | R5

## Slide 24: Stepping through an Array: Solution 2: Pointer Arithmetic
Maintain pointer to A[i] in a register
  Initialization: R4 = Address of A[0]
      Load R4, #A
Body of Loop:
      Load R3, (R4) # R3 = A[i]
      Add R3, R3, #1
      Store R3, (R4) # A[i] = A[i]+1
      Add R4, R4, 4 # Update pointer to array element

## Slide 25: Array Processing: A Larger Example
Find the max of N numbers:
A[0], A[1], …, A[N-1].
HLL Code:
  Max = A[0]
  for i=1, i<N {
  if(A[i]>Max) Max = A[i]
  }

## Slide 26: HLL to Assembly Code
Intermediate Code
Max = A[0]
i = 1
Loop: if(!(A[i])>Max)) goto Skip
Max = A[i]
Skip: i = i+1
if(N>i) goto Loop
Max = A[0]
for i=1, i<N {
if(A[i]>Max) Max = A[i]
}
Move R3, #N
Load R3, (R3)
Move R5, #A
Load R1, (R5)
Move R2, #1
Loop: Add R5, R5, #4
Load R4, (R5)
Branch_if_(R1>=R4) Skip
Move R1, R4
Skip: Add R2, R2, #1
Branch_if_(R3>R2) Loop
Move R2, #Max
Store R1, (R2)
Assembly Code
Variable: | Max | i | #N = (Addr. N) | A[i] | #A= Addr. A[0]
Register | R1 | R2 | R3 | R4 | R5
Note: R2 is reused after the for loop
to store the address #Max

## Slide 27: Reading Assignment
For another example of array processing using a for loop:
  Read and study the LISTADD example, Section 2.4.3 (pp. 45–47) of the textbook.

## Slide 28: Loading Large Constants
In the last example, “Load R5, #A” cannot be a RISC ISA instruction if #A is an absolute 32-bit address. Why?
Because it is a pseudoinstruction that must be expanded to real instruction.
General problem, solved in RISC processors by assembling 32-bit constants in two parts: high and low, e.g.
    Load_high R5, #A31-16
    Add R5, R5, # A15-0

## Slide 29: Real Assembly Languages (§2.5)
Mnemonics (LD/ADD instead of Load/Add) used when programming specific computers
The mnemonics represent the OP codes
Assembly language is the set of mnemonics and rules for using them to write programs
The rules constitute the language syntax
Example: suffix ‘I’ to specify immediate mode ADDI R2, R3, 5 (instead of #5)

## Slide 30: Assembler Directives
Other information also needed to translate source program to object program
How should symbolic names be interpreted?
Where should instructions/data be placed?
Assembler directives provide this information
ORIGIN defines instruction/data start position
RESERVE and DATAWORD define data storage
EQU associates a name with a constant value

## Slide 32
Assembler Directive
Address Label
Pseudo-op
Operation
Operands
Register Operands
Memory Addresses
Assembled Machine Code
Immediate
Operand
Comment
Nios II
Assembly
Lang.

## Slide 33: Number Notation
Decimal numbers used as immediate values: ADDI R2, R3, 93
Assembler translates to binary representation
Programmer may also specify binary numbers: ADDI R2, R3, %01011101
Hexadecimal specification is also possible: ADDI R2, R3, 0x5D
Note that 93  10111012  5D16

## Slide 34: HLL vs. Assembly
Operations:
  HLL: on variables & constants
  Assembly: on registers & constants
Typing
  HLL: Typed variables – can’t add a number to a character string
  Assembly: Registers are not typed – operation determines how register contents are treated.
Staging of instructions and data
  HLL: Abstracted – programmer unaware of the need
  Assembly: Since program and data initially in memory, all instructions and data must be staged on the processor for interpretation and operation.

## Slide 35: Nios II Assembly Language (§B.1–B.6)

## Slide 36: Registers
Register names should always in lower-case in Nios II assembler
Other symbols, e.g. labels, are case-sensitive
r0 is constant 0
Don’t use r1 in your programs.
r2–r23 can be freely used as general-purpose regs.

## Slide 37: Addressing Modes

## Slide 38: Load/Store
Load
  Form
      ldw r2, 20(r3) /* Load word instruction */
  Can also apply to bytes and halfword (ldb, ldh)
  Can control sign extension for byte and halfword operand by using ldb (sign extended) or ldbu (sign not extended)
Store: Similarly

## Slide 39: Pseudoinstructions Move
mov ri, rj
movi ri, value-16 /* 16-bit value */
movui ri, value-16 /* unsigned */
movia ri, LABEL /* 32-bit value – typically an address */
  Assembler implements as:
      orhi ri, r0, LABEL_HIGH
      ori ri,ri, LABEL_LOW

## Slide 40: Branch and Jump
Form
  br LABEL
  beq ri, rj, LABEL
where LABEL is 16-bit offset relative to PC
Signed and Unsigned versions, e.g, beq and bequ
Full range of comparisons:
  beq, bne, bge, bgt, ble, plus their unsigned versions

## Slide 41: Pseudoinstructions
Move type already mentioned
Subtract-Immediate:
  subi ri, rj, value-16 == addi ri, rj, -value-16
Branch Greater Than Signed
  bgt ri, rj, LABEL == blt rj, ri, LABEL

## Slide 42: Assembler Directives
.org Value /* ORIGIN */
.equ LABEL, Value /* LABEL = Value */
.byte expression /* Places byte size data
  into memory */
  .halfword and .word work similarly
.skip size /* Reserves memory space */
.end /* End of source-code file */

## Slide 43: Example Assembly Program: Ch. 2 Notation vs. Nios II
movia r3, N /* addr. N */
ldw r3, (r3)
movia r5, A
ldw r6, (r5)
movi r2, 1
Loop: addi r5, r5, 4
ldw r4, (r5)
bge r6, r4, Skip
mov r6, r4
Skip: addi r2, r2, 1
bgt r3, r2, Loop
movia r2, Max
stw r6, (r2)
Chapter 2
Nios II
Note: R1 is mapped to r6 because r1 is reserved as an assembler temporary register in Nios II.
Move R3, #N
Load R3, (R3)
Move R5, #A
Load R1, (R5)
Move R2, #1
Loop: Add R5, R5, #4
Load R4, (R5)
Branch_if_(R1>=R4) Skip
Move R1, R4
Skip: Add R2, R2, #1
Branch_if_(R3>R2) Loop
Move R2, #Max
Store R1, (R2)

## Slide 44: Adding Data Segment
movia r3, N
ldw r3, (r3)
movia r5, A
ldw r6, (r5)
movi r2, 1
Loop: addi r5, r5, 4
ldw r4, (r5)
bge r6, r4, Skip
mov r6, r4
Skip: addi r2, r2, 1
bgt r3, r2, Loop
movia r2, Max
stw r6, (r2)
.org 2000 /* Optional */
Max: .skip 4 /* Reserve 4 bytes for Max */
N: .word 20 /* Reserve word for N, initialized to 20 */
A: .skip 80 /* Reserve 80 bytes, or 20 words, for array A */
Nios II

## Slide 45: Program Assembly & Execution
From source program, assembler generates machine-language object program
Assembler uses ORIGIN and other directives to determine address locations for code/data
For branches, assembler computes ±offset from present address (in PC) to branch target
Loader places object program in memory
Debugger can be used to trace execution

## Slide 46: Program Assembly Example
Consider two-pass assembly relative to starting address of 0:
  Pass 1 builds the symbol table
  Pass 2 generates code
movia r3, N
ldw r3, (r3)
movia r5, A
ldw r6, (r5)
movi r2, 1
Loop: addi r5, r5, 4
ldw r4, (r5)
bge r6, r4, Skip
mov r6, r4
Skip: addi r2, r2, 1
bgt r3, r2, Loop
movia r2, Max
stw r6, (r2)
.org 2000
Max: .skip 4
N: .word 20
A: .skip 80

## Slide 47: Pass 1
0 movia r3, N
ldw r3, (r3)
movia r5, A
ldw r6, (r5)
movi r2, 1
Loop: addi r5, r5, 4
ldw r4, (r5)
bge r6, r4, Skip
mov r6, r4
Skip: addi r2, r2, 1
bgt r3, r2, Loop
movia r2, Max
stw r6, (r2)
.org 2000
Max: .skip 4
N: .word 20
A: .skip 80
Symbol | Value
N | undefined
Symbol Table

## Slide 48: Pass 1
0 movia r3, N
4 ldw r3, (r3)
8 movia r5, A
ldw r6, (r5)
movi r2, 1
Loop: addi r5, r5, 4
ldw r4, (r5)
bge r6, r4, Skip
mov r6, r4
Skip: addi r2, r2, 1
bgt r3, r2, Loop
movia r2, Max
stw r6, (r2)
.org 2000
Max: .skip 4
N: .word 20
A: .skip 80
Symbol | Value
N | undefined
A | undefined
Symbol Table

## Slide 49: Pass 1
0 movia r3, N
4 ldw r3, (r3)
8 movia r5, A
12 ldw r6, (r5)
16 movi r2, 1
20 Loop: addi r5, r5, 4
ldw r4, (r5)
bge r6, r4, Skip
mov r6, r4
Skip: addi r2, r2, 1
bgt r3, r2, Loop
movia r2, Max
stw r6, (r2)
.org 2000
Max: .skip 4
N: .word 20
A: .skip 80
Symbol | Value
N | undefined
A | undefined
Loop | 20
Symbol Table

## Slide 50: Pass 1
0 movia r3, N
4 ldw r3, (r3)
8 movia r5, A
12 ldw r6, (r5)
16 movi r2, 1
20: addi r5, r5, 4
24 ldw r4, (r5)
28 bge r6, r4, Skip
mov r6, r4
Skip: addi r2, r2, 1
bgt r3, r2, Loop
movia r2, Max
stw r6, (r2)
.org 2000
Max: .skip 4
N: .word 20
A: .skip 80
Symbol | Value
N | undefined
A | undefined
Loop | 20
Skip | undefined
Symbol Table

## Slide 51: Pass 1
0 movia r3, N
4 ldw r3, (r3)
8 movia r5, A
12 ldw r6, (r5)
16 movi r2, 1
20: addi r5, r5, 4
24 ldw r4, (r5)
28 bge r6, r4, Skip
32 mov r6, r4
36 Skip: addi r2, r2, 1
bgt r3, r2, Loop
movia r2, Max
stw r6, (r2)
.org 2000
Max: .skip 4
N: .word 20
A: .skip 80
Symbol | Value
N | undefined
A | undefined
Loop | 20
Skip | undefined -> 36
Symbol Table

## Slide 52: Pass 1
0 movia r3, N
4 ldw r3, (r3)
8 movia r5, A
12 ldw r6, (r5)
16 movi r2, 1
20: addi r5, r5, 4
24 ldw r4, (r5)
28 bge r6, r4, Skip
32 mov r6, r4
36: addi r2, r2, 1
40 bgt r3, r2, Loop20
movia r2, Max
stw r6, (r2)
.org 2000
Max: .skip 4
N: .word 20
A: .skip 80
Symbol | Value
N | undefined
A | undefined
Loop | 20
Skip | 36
Symbol Table

## Slide 53: Pass 1
0 movia r3, N
4 ldw r3, (r3)
8 movia r5, A
12 ldw r6, (r5)
16 movi r2, 1
20: addi r5, r5, 4
24 ldw r4, (r5)
28 bge r6, r4, Skip
32 mov r6, r4
36: addi r2, r2, 1
40 bgt r3, r2, 20
44 movia r2, Max
stw r6, (r2)
.org 2000
Max: .skip 4
N: .word 20
A: .skip 80
Symbol | Value
N | undefined
A | undefined
Loop | 20
Skip | 36
Max | undefined
Symbol Table

## Slide 54: Pass 1
0 movia r3, N
4 ldw r3, (r3)
8 movia r5, A
12 ldw r6, (r5)
16 movi r2, 1
20: addi r5, r5, 4
24 ldw r4, (r5)
28 bge r6, r4, Skip
32 mov r6, r4
36: addi r2, r2, 1
40 bgt r3, r2, 20
44 movia r2, Max
stw r6, (r2)
.org 2000
2000 Max: .skip 4
N: .word 20
A: .skip 80
Symbol | Value
N | undefined
A | undefined
Loop | 20
Skip | 36
Max | undefined ->2000
Symbol Table

## Slide 55: Pass 1
0 movia r3, N
4 ldw r3, (r3)
8 movia r5, A
12 ldw r6, (r5)
16 movi r2, 1
20 : addi r5, r5, 4
24 ldw r4, (r5)
28 bge r6, r4, Skip
32 mov r6, r4
36: addi r2, r2, 1
40 bgt r3, r2, 20
44 movia r2, Max
stw r6, (r2)
.org 2000
2000: .skip 4
2004: N .word 20
A: .skip 80
Symbol | Value
N | undefined ->2004
A | undefined
Loop | 20
Skip | 36
Max | 2000
Symbol Table

## Slide 56: Pass 1
0 movia r3, N
4 ldw r3, (r3)
8 movia r5, A
12 ldw r6, (r5)
16 movi r2, 1
20: addi r5, r5, 4
24 ldw r4, (r5)
28 bge r6, r4, Skip
32 mov r6, r4
36: addi r2, r2, 1
40 bgt r3, r2, 20
44 movia r2, Max
stw r6, (r2)
.org 2000
2000: .skip 4
2004: .word 20
2008 A: .skip 80
2088 …
Symbol | Value
N | 2004
A | undefined->2008
Loop | 20
Skip | 36
Max | 2000
Symbol Table

## Slide 57: Pass 1
0 movia r3, N
4 ldw r3, (r3)
8 movia r5, A
12 ldw r6, (r5)
16 movi r2, 1
20: addi r5, r5, 4
24 ldw r4, (r5)
28 bge r6, r4, Skip
32 mov r6, r4
36: addi r2, r2, 1
40 bgt r3, r2, 20
44 movia r2, Max
stw r6, (r2)
.org 2000
2000: .skip 4
2004: .word 20
2008: .skip 80
2088 …
Symbol | Value
N | 2004
A | 2008
Loop | 20
Skip | 36
Max | 2000
Symbol Table

## Slide 58: Pass 2
0 movia r3, N 2004
4 ldw r3, (r3)
8 movia r5, A
12 ldw r6, (r5)
16 movi r2, 1
20: addi r5, r5, 4
24 ldw r4, (r5)
28 bge r6, r4, Skip
32 mov r6, r4
36: addi r2, r2, 1
40 bgt r3, r2, 20
44 movia r2, Max
stw r6, (r2)
.org 2000
2000: .skip 4
2004: .word 20
2008: .skip 80
2088 …
Symbol | Value
N | 2004
A | 2008
Loop | 20
Skip | 36
Max | 2000
Symbol Table

## Slide 59: Pass 2
0 movia r3, 2004
4 ldw r3, (r3)
8 movia r5, A2008
12 ldw r6, (r5)
16 movi r2, 1
20: addi r5, r5, 4
24 ldw r4, (r5)
28 bge r6, r4, Skip
32 mov r6, r4
36: addi r2, r2, 1
40 bgt r3, r2, 20
44 movia r2, Max
stw r6, (r2)
.org 2000
2000: .skip 4
2004: .word 20
2008: .skip 80
2088 …
Symbol | Value
N | 2004
A | 2008
Loop | 20
Skip | 36
Max | 2000
Symbol Table

## Slide 60: Pass 2
0 movia r3, 2004
4 ldw r3, (r3)
8 movia r5, 2008
12 ldw r6, (r5)
16 movi r2, 1
20: addi r5, r5, 4
24 ldw r4, (r5)
28 bge r6, r4, Skip36
32 mov r6, r4
36: addi r2, r2, 1
40 bgt r3, r2, 20
44 movia r2, Max
stw r6, (r2)
.org 2000
2000: .skip 4
2004: .word 20
2008 A: .skip 80
2088 …
Symbol | Value
N | 2004
A | 2008
Loop | 20
Skip | 36
Max | 2000
Symbol Table

## Slide 61: Pass 2
0 movia r3, 2004
4 ldw r3, (r3)
8 movia r5, 2008
12 ldw r6, (r5)
16 movi r2, 1
20: addi r5, r5, 4
24 ldw r4, (r5)
28 bge r6, r4, 36
32 mov r6, r4
36: addi r2, r2, 1
40 bgt r3, r2, 20
44 movia r2, Max2000
stw r6, (r2)
.org 2000
2000: .skip 4
2004: .word 20
2008 A: .skip 80
2088 …
Symbol | Value
N | 2004
A | 2008
Loop | 20
Skip | 36
Max | 2000
Symbol Table

## Slide 62: Pass 2
0 movia r3, 2004
4 ldw r3, (r3)
8 movia r5, 2008
12 ldw r6, (r5)
16 movi r2, 1
20: addi r5, r5, 4
24 ldw r4, (r5)
28 bge r6, r4, 36
32 mov r6, r4
36: addi r2, r2, 1
40 bgt r3, r2, 20
44 movia r2, 2000
stw r6, (r2)
.org 2000
2000: .skip 4
2004: .word 20
2008 A: .skip 80
2088 …
Symbol | Value
N | 2004
A | 2008
Loop | 20
Skip | 36
Max | 2000
Symbol Table