## Slide 1: CSCE 230, Fall 2013 Chapter 5: Basic Processing Unit Part 2: Control Unit
Mehmet Can Vuran, Instructor
University of Nebraska-Lincoln
Acknowledgement: Overheads adapted from those provided by the authors of the textbook

## Slide 2: Processor control section
When an instruction is read, it is placed in IR.
The control circuitry decodes the instruction.
It generates the control signals that drive all units.
The Immediate block extends the immediate operand to 32 bits as specified in the instruction.

## Slide 3: Control signal generation
There are two basic approaches: hardwired control and microprogramming
Hardwired control involves implementing circuitry that considers step counter, IR, ALU result, and external inputs. Step counter keeps track of execution progress, one clock cycle for each of the five steps described earlier.
Microprogramming involves creating another layer of interpretation, below ISA, for interpreting each ISA instruction.

## Slide 4: Hardwired generation of control signals

## Slide 5
Datapath + Control

## Slide 6
Stage 1: Instruction Fetch
  Address = PC,
  PC = PC+4
MA_select = 1
MEM_read
INC_select =0
PC_select = 1
PC_enable
  if(MFC=1) IR = MemData
if(MFC) IR_enable = 1

## Slide 7
Stage 2: Instruction Decode
Instruction in IR decoded by the Control Unit logic (not shown)
Source-register fields in IR (IR31-27 and IR26-22) determine Address A and Address B of Register File.

## Slide 8
Stages 2-5: R-Type
Stage 2:
  RA = RegFile[AddressA],
  RB = RegFile[AddressB]
(These and other buffer registers can be enabled for every clock cycle so no enable signals necessary)
Stage 3:
  RZ = [RA] op [RB]
B_select = 0,
ALU_op = op
Stage 4:
  RY = [RZ]
Y_select = 0
Stage 5:
  RegFile[AddressC] = RY
RF_write = 1
C_select = 01

## Slide 9
Stages 2-5: Load Inst.
Stage 2:
  RA = RegFile[AddressA],
  RB = RegFile[AddressB]
Stage 3:
  RZ = [RA] op Immediate
B_select = 1,
ALU_op = Add
Stage 4:
  Memory address = [RZ]
MA_select = 0
MEM_read
  if(MFC=1) RY= MemData
  if(MFC) Y_select = 1
Stage 5:
  RegFile[AddressC] = RY
RF_write = 1
C_select = 00

## Slide 10
Stages 2-5: Store Inst.
Stage 2:
  RA = RegFile[AddressA],
  RB = RegFile[AddressB]
Stage 3:
  RZ = [RA] op Immediate
  RM = [RB]
B_select = 1,
ALU_op = Add
Stage 4:
  Memory address = [RZ]
  Memory data = [RM]
MA_select = 0
MEM_write
  while(!MFC)
  Wait for MFC
Stage 5: Idle

## Slide 11
Stages 2-5: Call Inst.
Assume the Immediate block extends the 26-bit immediate value in the instruction to 32-bits Immediate Value (address of the called routine).
If Fetch and Decode stages remain unchanged, we must do the following operations in the remaining stages:
PC-Temp = PC,
PC = Immediate Value
Link-Reg = PC-Temp
We will discuss why these operations cannot be completed in the given datapath and consider solutions to the problem.
Must change datapath for absolute calls

## Slide 12
Stages 2-5: Call Inst.
Solution 1
Fetch
Decode
PC-Temp=PC,
PC=Immediate value
RY=PC-Temp
Register-LINK=RY
This solution requires modifying data path to allow Immediate value to be loaded in PC in Step 3. This can be done by including a third input to MuxPC from Immediate value.

## Slide 13
Stages 2-5: Call Inst.
Solution 2
Fetch
Decode, RA = Immediate value
PC-Temp=PC, PC=RA
RY=PC-Temp
Register-LINK=RY
This solution also requires modifying the data path for Step 2: introduce a mux at the input of RA to allow Immediate value to be loaded to RA.
Q: Which solution is better?
A: Most likely, Solution 1 because it does not extra delay in the Register File to RA path that is used by most instructions.

## Slide 14: In-class Exercise
Clock Cycle

## Slide 15: What is the delay in each stage?
Component delays
  Control – 100ps
  Mem – 350ps
  Add – 100ps
  Mux – 30ps
  ALU – 120ps
  Reg File – 200ps
  Sign-extend – 20ps
  Reg (write) – 10ps
  Reg (read) – 0 ps
Fetch
R-format
Load/store
Unconditional PC-relative branch
Conditional PC-relative branch

## Slide 16
Datapath + Control

## Slide 17
Stage/Instruction |  |  |  |  |  |  |  |  | Delay
Fetch | MuxMA | MEM | IR | Add | MuxPC | PC |  |  | 
 | 30 | 350 | 10 | 100 | 30 | 10 |  |  | 530
Fetch | MuxMA | MEM | IR |  |  |  |  |  | 
(Optimized) | 30 | 350 | 10 |  |  |  |  |  | 390
 | MuxINC | Add | PC |  |  |  |  |  | 
 | 30 | 100 | 10 |  |  |  |  |  | 
Decode | RegFile | RA/RB |  |  |  |  |  |  | 
 | 200 | 10 |  |  |  |  |  |  | 210
 | Control |  |  |  |  |  |  |  | 
 | 100 |  |  |  |  |  |  |  | 

## Slide 18
Stage/Instruction |  |  |  |  |  |  |  |  | Delay
EXE |  |  |  |  |  |  |  |  | 
R-Type | MuxB | ALU | RZ |  |  |  |  |  | 
 | 30 | 120 | 10 |  |  |  |  |  | 160
Load/St | MuxB | ALU | RZ |  |  |  |  |  | 
 | 30 | 120 | 10 |  |  |  |  |  | 160
Uncond. Branch | MuxINC | Adder | MuxPC | PC |  |  |  |  | 
 | 30 | 100 | 30 | 10 |  |  |  |  | 170
Cond. PC-rel Branch | MuxB | ALU | Control | MuxINC | Adder | MuxPC | PC |  | 
 | 30 | 120 | 100 | 30 | 100 | 30 | 10 |  | 420

## Slide 19
Stage/Instruction |  |  |  |  |  |  |  |  | Delay
MEM |  |  |  |  |  |  |  |  | 
Load | MuxMA | MEM | MuxY | RY |  |  |  |  | 
 | 30 | 350 | 30 | 10 |  |  |  |  | 420
R-Type | MuxY | RY |  |  |  |  |  |  | 
 | 30 | 10 |  |  |  |  |  |  | 40
Branch | MuxY | RY |  |  |  |  |  |  | 
 | 30 | 10 |  |  |  |  |  |  | 40
WB | MuxC | RegFile |  |  |  |  |  |  | 
 | 30 | 200 |  |  |  |  |  |  | 230

## Slide 20: Hardwired generation of control signals

## Slide 21: Step Counter FSM Description
Stage time determined by the longest stage delay.
For all but Stage-4 time, the processor design can determine the longest stage delay by analysis of inter-stage logic.
The time for the Memory stage for memory instructions (load and store), depends on the time to complete the requested memory operation
For maximum flexibility asynchronous communication may be used, i.e.
  create a wait for memory function completion (WMFC) signal, asserted to 1 in Stage 4 if read/write requested; the Memory Unit signals completion by asserting MFC.
Hence the Stage counter is enabled whenever the WFMC is not asserted. Otherwise it is enabled when the memory function complete signal is received.
    Counter_enable = WMFC’ + MFC

## Slide 22: Control Unit Logic – General Principles
Two ways to describe:
  For each instruction determine which control signals must be activated, i.e
    if(Instruction=INSi) then (list of active control signals by stages)
    This is like a truth table specification of the control signals, we have considered many examples already.
  For each control signal, determine the Boolean condition which captures all the cases under which it is active.
  This is like synthesizing the logic of each control signal from the truth-table specification

## Slide 23: Control Unit Logic: 5-Stage Hardwired Control
Two ways to analyze:
  Focus on each instruction and contingency (like interrupt):
    if (Instruction = INSi, and step counter = Tj, and Condition signals = …, and External input = ...) then (list of active signals for the if condition)
    This is essentially specifying the truth tables of the control signals and we let a synthesis program figure out the logic for each control signal.
  Focus on control signals. For each control signal (or group), write conditions based on instructions (or instruction types), Step counter value (T1 through T5), condition signals (NZVC, MFC, …), and external inputs (interrupt signals) to determine when that particular signal should be activated. (This is harder to do)

## Slide 24: Example (Hardwired Control)
Describe the conditions under which C_select will be active to specify destination register?
Consider the three cases for C_select = 0, 1, and 2.
  IR21-17 for Register-operand instructions
  IR26-22 for Immediate-operand instructions
  LINK for Call type of instructions.
For reference the instruction formats
are reproduced on the next slide.
Notes: C_select is 0 for all immediate instructions, 1 for all computational instructions with both operands in registers, and 2 for all link instructions.

## Slide 25: Instruction Formats (Chapter 5 Processor)
Fig. 5.12

## Slide 26: Reading Assignment
Review all the solved problems in Section 5.9 that include several other examples of datapath and control logic design.

## Slide 27: In-class Exercise
Control Implementation

## Slide 28: Control Implementation
Divide into two parts
  ALU Control
  The rest

## Slide 29: ALU
00
01
10
MUX
R
G
ALU
B
A
R
C
F,G
F | G1 | G0 | R
- | 0 | 0 | And
- | 0 | 1 | Or
0 | 1 | 0 | Add
1 | 1 | 0 | Sub
- | 1 | 1 | -
B
A
F
C
Basic
ALU
B
A
B
A
AND
OR
ADD/
SUB

## Slide 30: Control Design
23 |  |  | 20 | 19 | 18 |  | 16 | 15 |  |  | 12 | 11 |  |  | 8 | 7 |  |  | 4 | 3 |  |  | 0
Cond |  |  |  | S | opx |  |  | rd |  |  |  | rt |  |  |  | rs |  |  |  | 0 | 0 | 0 | 0
R-Type
23 |  |  | 20 | 19 | 18 |  |  |  |  |  | 12 | 11 |  |  | 8 | 7 |  |  | 4 | 3 |  |  | 0
Cond |  |  |  | S | Imm |  |  |  |  |  |  | rd |  |  |  | rs |  |  |  | 0 | 1 | X | X
D-Type
Based on the following ISA
  R-type (add, sub, or, and), lw, sw

## Slide 31: ALU Control
Based on the following ISA
  R-type (add, sub, or, and), lw, sw
instruction | op | Operation | Opx | ALU function | ALU control
lw | 0100 | load word | XXX | add | 010
sw | 0101 | store word | XXX | add | 010
R-type | 0000 | add | 010 | add | 010
 |  | subtract | 000 | subtract | 110
 |  | AND | 101 | AND | X00
 |  | OR | 100 | OR | X01

## Slide 32: ALU Control
Op |  |  |  | opx |  |  | ALU Control |  | 
op3 | op2 | op1 | op0 | opx2 | opx1 | opx0 | F | G1 | G0

## Slide 33: ALU Control
Op |  |  |  | opx |  |  | ALU Control |  | 
op3 | op2 | op1 | op0 | opx2 | opx1 | opx0 | F | G1 | G0
0 | 1 | 0 | 0 | X | X | X | 0 | 1 | 0
0 | 1 | 0 | 1 | X | X | X | 0 | 1 | 0
0 | 0 | 0 | 0 | 0 | 1 | 0 | 0 | 1 | 0
0 | 0 | 0 | 0 | 0 | 0 | 0 | 1 | 1 | 0
0 | 0 | 0 | 0 | 1 | 0 | 1 | X | 0 | 0
0 | 0 | 0 | 0 | 1 | 0 | 0 | X | 0 | 1

## Slide 34: ALU Control
op |  |  |  | opx |  |  | ALU Control |  | 
op3 | op2 | op1 | op0 | opx2 | opx1 | opx0 | F | G1 | G0
0 | 1 | 0 | 0 | X | X | X | 0 | 1 | 0
0 | 1 | 0 | 1 | X | X | X | 0 | 1 | 0
0 | 0 | 0 | 0 | 0 | 1 | 0 | 0 | 1 | 0
0 | 0 | 0 | 0 | 0 | 0 | 0 | 1 | 1 | 0
0 | 0 | 0 | 0 | 1 | 0 | 1 | X | 0 | 0
0 | 0 | 0 | 0 | 1 | 0 | 0 | X | 0 | 1
G0

## Slide 35: ALU Control
op |  |  |  | opx |  |  | ALU Control |  | 
op3 | op2 | op1 | op0 | opx2 | opx1 | opx0 | F | G1 | G0
0 | 1 | 0 | 0 | X | X | X | 0 | 1 | 0
0 | 1 | 0 | 1 | X | X | X | 0 | 1 | 0
0 | 0 | 0 | 0 | 0 | 1 | 0 | 0 | 1 | 0
0 | 0 | 0 | 0 | 0 | 0 | 0 | 1 | 1 | 0
0 | 0 | 0 | 0 | 1 | 0 | 1 | X | 0 | 0
0 | 0 | 0 | 0 | 1 | 0 | 0 | X | 0 | 1
G0

## Slide 36: ALU Control
op |  |  |  | opx |  |  | ALU Control |  | 
op3 | op2 | op1 | op0 | opx2 | opx1 | opx0 | F | G1 | G0
0 | 1 | 0 | 0 | X | X | X | 0 | 1 | 0
0 | 1 | 0 | 1 | X | X | X | 0 | 1 | 0
0 | 0 | 0 | 0 | 0 | 1 | 0 | 0 | 1 | 0
0 | 0 | 0 | 0 | 0 | 0 | 0 | 1 | 1 | 0
0 | 0 | 0 | 0 | 1 | 0 | 1 | X | 0 | 0
0 | 0 | 0 | 0 | 1 | 0 | 0 | X | 0 | 1
G1

## Slide 37: ALU Control
op |  |  |  | opx |  |  | ALU Control |  | 
op3 | op2 | op1 | op0 | opx2 | opx1 | opx0 | F | G1 | G0
0 | 1 | 0 | 0 | X | X | X | 0 | 1 | 0
0 | 1 | 0 | 1 | X | X | X | 0 | 1 | 0
0 | 0 | 0 | 0 | 0 | 1 | 0 | 0 | 1 | 0
0 | 0 | 0 | 0 | 0 | 0 | 0 | 1 | 1 | 0
0 | 0 | 0 | 0 | 1 | 0 | 1 | X | 0 | 0
0 | 0 | 0 | 0 | 1 | 0 | 0 | X | 0 | 1
G1

## Slide 38: ALU Control
op |  |  |  | opx |  |  | ALU Control |  | 
op3 | op2 | op1 | op0 | opx2 | opx1 | opx0 | F | G1 | G0
0 | 1 | 0 | 0 | X | X | X | 0 | 1 | 0
0 | 1 | 0 | 1 | X | X | X | 0 | 1 | 0
0 | 0 | 0 | 0 | 0 | 1 | 0 | 0 | 1 | 0
0 | 0 | 0 | 0 | 0 | 0 | 0 | 1 | 1 | 0
0 | 0 | 0 | 0 | 1 | 0 | 1 | X | 0 | 0
0 | 0 | 0 | 0 | 1 | 0 | 0 | X | 0 | 1
F

## Slide 39: ALU Control
op |  |  |  | opx |  |  | ALU Control |  | 
op3 | op2 | op1 | op0 | opx2 | opx1 | opx0 | F | G1 | G0
0 | 1 | 0 | 0 | X | X | X | 0 | 1 | 0
0 | 1 | 0 | 1 | X | X | X | 0 | 1 | 0
0 | 0 | 0 | 0 | 0 | 1 | 0 | 0 | 1 | 0
0 | 0 | 0 | 0 | 0 | 0 | 0 | 1 | 1 | 0
0 | 0 | 0 | 0 | 1 | 0 | 1 | X | 0 | 0
0 | 0 | 0 | 0 | 1 | 0 | 0 | X | 0 | 1
F

## Slide 40: ALU Control
op (3-0)
op2
opx (2-0)
opx2
opx1
opx0
G0
G1
F

## Slide 41: Control Design (limited edition)
Limited to
  Stages 3,4,5
  R-type (add, sub, or, and), lw, sw
  Control signals on ALU path and Proc-Mem interface path (PC path omitted)
Immediate control
  00 – sign-extend 7-bit Immediate field (IR18-12)
  01 – 0-extend 7-bit immediate field (IR18-12)
  10 – sign-extend 16-bit label field (IR19-4)
  11 – 0-extend 20-bit Const field (IR23-4)
Inter-stage registers hold value during a stage

## Slide 42: Control Hardware

## Slide 43
Datapath + Control

## Slide 44: Control Design (limited edition)
R-Type | T3 | T4 | T5 | RF_write | C_select |  | B_select | Y_select |  | MEM_read | MEM_write | MA_select | Extend | 
 |  |  |  |  | C1 | C0 |  | Y1 | Y0 |  |  |  | E1 | E0
0000 | 1 | 0 | 0 | 0 | X | X | 0 | X | X | 0 | 0 | X | X | X
0000 | 0 | 1 | 0 | 0 | X | X | X | 0 | 0 | 0 | 0 | X | X | X
0000 | 0 | 0 | 1 | 1 | 0 | 1 | X | X | X | 0 | 0 | X | X | X

## Slide 45: Control Design (limited edition)
 | T3 | T4 | T5 | RF_write | C_select |  | B_select | Y_select |  | MEM_read | MEM_write | MA_select | Extend | 
 |  |  |  |  | C1 | C0 |  | Y1 | Y0 |  |  |  | E1 | E0

## Slide 46: Control Design (limited edition)
lw | T3 | T4 | T5 | RF_write | C_select |  | B_select | Y_select |  | MEM_read | MEM_write | MA_select | Extend | 
 |  |  |  |  | C1 | C0 |  | Y1 | Y0 |  |  |  | E1 | E0
0100 | 1 | 0 | 0 | 0 | X | X | 1 | X | X | 0 | 0 | X | 0 | 0
0100 | 0 | 1 | 0 | 0 | X | X | X | 0 | 1 | 1 | 0 | 0 | X | X
0100 | 0 | 0 | 1 | 1 | 0 | 0 | X | X | X | 0 | 0 | X | X | X

## Slide 47: Control Design (limited edition)
sw | T3 | T4 | T5 | RF_write | C_select |  | B_select | Y_select |  | MEM_read | MEM_write | MA_select | Extend | 
 |  |  |  |  | C1 | C0 |  | Y1 | Y0 |  |  |  | E1 | E0
0101 | 1 | 0 | 0 | 0 | X | X | 1 | X | X | 0 | 0 | X | 0 | 0
0101 | 0 | 1 | 0 | 0 | X | X | X | X | X | 0 | 1 | 0 | X | X
0101 | 0 | 0 | 1 | 0 | X | X | X | X | X | 0 | 0 | X | X | X

## Slide 48: Control Truth Table (LE)
Input or Output | Signal Name | R(3) | R(4) | R(5) | lw(3) | lw(4) | lw(5) | sw(3) | sw(4) | sw(5)
Inputs | op3 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0
 | op2 | 0 | 0 | 0 | 1 | 1 | 1 | 1 | 1 | 1
 | op1 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0
 | op0 | 0 | 0 | 0 | 0 | 0 | 0 | 1 | 1 | 1
 | T3 | 1 | 0 | 0 | 1 | 0 | 0 | 1 | 0 | 0
 | T4 | 0 | 1 | 0 | 0 | 1 | 0 | 0 | 1 | 0
 | T5 | 0 | 0 | 1 | 0 | 0 | 1 | 0 | 0 | 1
Outputs | RF_write | 0 | 0 | 1 | 0 | 0 | 1 | 0 | 0 | 0
 | C_select (C1) | X | X | 0 | X | X | 0 | X | X | X
 | C_select (C0) | X | X | 1 | X | X | 0 | X | X | X
 | B_select | 0 | X | X | 1 | X | X | 1 | X | X
 | Y_select (Y1) | X | 0 | X | X | 0 | X | X | X | X
 | Y_select (Y0) | X | 0 | X | X | 1 | X | X | X | X
 | MEM_read | 0 | 0 | 0 | 0 | 1 | 0 | 0 | 0 | 0
 | MEM_write | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 1 | 0
 | MA_select | X | X | X | X | 0 | X | X | 0 | X
 | Extend (E1) | X | X | X | 0 | X | X | 0 | X | X
 | Extend (E0) | X | X | X | 0 | X | X | 0 | X | X

## Slide 49
RF_write
C_select (C1)
C_select (C0)
B_select
Y_select (Y1)
Y_select (Y0)
MEM_read
MEM_write
MA_select
Extend (E1)
Extend (E0)
op3
op2
op1
op0
T3
T4
T5
R(3)
R(4)
R(5)
lw(3)
lw(4)
lw(5)
sw(3)
sw(4)
sw(5)
0

## Slide 50: ARM – Conditional Execution

## Slide 51: Conditional Execution in ARM
Most instruction sets only allow branches to be executed conditionally
ARM ISA is described in Appendix D
  Several documents on ARM are on BB
Conditional execution of instructions:
  All instructions, including branches, are executed conditionally, based on a 4-bit condition field value in each instruction
Project processor borrows this concept from ARM

## Slide 52
S

## Slide 54: Register Structure in ARM
Sixteen 32-bit processor registers, labeled R0 through R15
Register R15 is the program counter (PC)
Registers R13 and R14 have dedicated uses related to subroutine and processor stack management
A current program status register (CPSR) holds the condition code flags (N, Z, C, V), two interrupt-disable bits, and five processor mode bits

## Slide 56: Conditional Instructions
Instruction behavior changes based on the status of the condition flags
Different (15) types of instructions can be generated from a single instruction with the use of conditions
  By reusing the condition evaluation hardware, ARM effectively increases number of instructions.
All instructions contain a condition field which determines whether the CPU will execute them.
  Non-executed instructions soak up 1 cycle.
Still have to complete cycle so as to allow fetching and decoding of following instructions.

## Slide 57: Conditional Instructions
Branch: B{condition} LOCATION branches to LOCATION if the settings of the condition code flags satisfy {condition} BEQ LOCATION branches if Z  1

## Slide 59: Condition Flags
Each instruction checks the CPSR register to see if the instruction conditions match CPSR conditions
e.g. ADDEQ r0,r1,r2
  If zero flag set then… r0 = r1 + r2
  Check CPSR
    If Z==1, execute
    Else, nop
e.g., ADD r0, r1, r2
  = ADDAL r0, r2, r2
  Always execute, no need to check CPSR

## Slide 60: Condition Flags
How is CPSR set?
  S field
  Compare instructions

## Slide 61: Condition Flags (S Field)
By default, data processing operations do not affect the condition flags (apart from the comparisons where this is the only effect)
  E.g., ADD ro, r1, r2
  Does NOT affect CPSR (condition signals are still generated by ALU but to no effect)
To cause the condition flags to be updated, the S bit of the instruction needs to be set by postfixing the instruction (and any condition code) with an “S”.
  e.g., ADDS r0,r1,r2
  Perform r0 = r1 + r2 and set flags based on the result

## Slide 62: Condition Flags (Compare)
The only effect of the comparisons is to
  UPDATE THE CONDITION FLAGS
  No need to set S bit.
Operations in ARM:
  CMP operand1 - operand2, but result not written
  CMN operand1 + operand2, but result not written
  TST operand1 AND operand2, but result not written
  TEQ operand1 EOR operand2, but result not written
Syntax:
  <Operation>{<cond>} Rn, Operand2
Examples:
  CMP r0, r1
  TSTEQ r2, #5

## Slide 63: Typical ARM Instruction
<Operation>{<cond>}{S} Rd, Rn, Operand2
  Lack of <cond>  AL
  Lack of S  S=0

## Slide 64: Example
MOVS ro, r1
MOVEQS r0, r2
MOVEQ r0, r3
1st instruction
  Moves r1 to r0 unconditionally
  Sets the condition flags
  Z flag is set if r1=0
2nd instruction
  Executed only if Z=1 (r1=0)
  Moves r2 to r0
  Sets the condition flags
  Z flag is set if r2=0
3rd instruction
  Executed only if Z=1 (r2=0)
  Moves r3 to r0
  Condition flags are not set
3rd instruction is executed only if r1=0 and r2=0

## Slide 65: Summary
Covered main concepts of designing a basic processor in class.
Some real features of modern processors not yet covered: pipelining, floating point, memory hierarchy, multi-core processors (aka chip multiprocessors or CMPs).
Some of these will be covered in the coming weeks.