## Slide 1
ECE 383 – Embedded Computer Systems II Lecture 19 – Soft Core (MicroBlaze) + Custom IP with Interrupt
1
Maj Jeffrey Falkinburg Room 2E46E 333-9193

## Slide 2: Lesson Outline
Time Logs!
MicroBlaze + Custom IP with Interrupt

## Slide 3: MicroBlaze + Custom IP with Interrupt

## Slide 4: MicroBlaze + Custom IP with Interrupt
axi_uartlite_0 @ 40600000
S_AXI_ACLK
S_AXI_ARESETN
slv_reg1
clk
reset_n
ctrl
Artix 7 (design_1)
MicroBlaze
my_counter_ip_v2_0.vhd @ 0x44a00000
my_counter_ip_v2_0_S00_AXI.vhd
Lec19.vhd
32
slv_reg0
Q/D
32
Lec18.xdc
8
LED
T14
T15
T16
U16
V15
W16
W15
Y13
Design_1.xdc
AA19
V18
RX
RX
TX
TX
clk
reset_n
R4
G4
roll
myISR()
main()
slv_reg2
Lec19.c
Interrupt
axi_lite
slv_reg3
flagQ
set
clear

## Slide 5: MicroBlaze + Custom IP – Workflow
The work flow has three main steps.
  Define a new hardware design (MicroBlaze + axi_uartlite) in Vivado IP Integrator (using the MicroBlaze Tutorial from Lecture 17)
  Create and package new custom IP (your custom hardware) and import it into your Vivado design
  Program the resulting hardware in the SDK environment.
Lets start with the first step.

## Slide 6: Xilinx Vivado – IP Integrator
  This step requires that you start a new hardware design (MicroBlaze + axi_uartlite) in Vivado IP Integrator in a new project called Lecture_19.
  You will add a new Block Design with a MicroBlaze and axi_uartlite following the MicroBlaze Tutorial.
http://ece.ninja/383/hand/Nexys_Video_MicroBlaze_Tutorial.pdf
***Deviation from Lecture 17 Tutorial***
  Do not include the MicroBlaze Interrupt Controller check box.
  If you do you could probably delete it from your design

## Slide 7: Xilinx Vivado – IP Integrator
  This step requires that you start a new hardware design (MicroBlaze + axi_uartlite) in Vivado IP Integrator in a new project called Lecture_19.
  You will add a new Block Design with a MicroBlaze and axi_uartlite following the MicroBlaze Tutorial.
http://ece.ninja/383/hand/Nexys_Video_MicroBlaze_Tutorial.pdf
***Deviation from Lecture 17 Tutorial***
  Do not include the MicroBlaze Interrupt Controller check box.
  If you do you could probably delete it from your design
Don’t Select!

## Slide 8: IP Catalog – Adding IP Repo
Open IP Catalog Settings and click on Repository Manager and add your IP Repo to your IP Repositories
  /path_to_ip_repo/git_repo/ip_repo
1

## Slide 9: Edit/Create New IP Package
Edit Counter in IP Packager or create a new IP package
I chose to create a new package with a new version.

## Slide 10: Edit/Create New IP Package
Expose the Roll Signal to the Artix 7 (design_1) block diagram by following the LED port maps

## Slide 11: Xilinx Vivado – Create and Package Custom IP
8. Add Custom IP to your design
  8.1) In the project manager page of the original window, click Open Block Design. This adds a block design to the project.
  8.2) Use the Add IP button to add our v2.0 of our Lec 10 Counter IP Core with the exposed roll signal.
Notice it is v2.0

## Slide 12: Edit/Create New IP Package
Click the ‘+’ sign by the MicroBlaze to connect the Roll Signal to the MicroBlaze Interrupt input directly
1
2
3

## Slide 13: Verify Design
You should verify the addressing for all your design components before continuing.
Verify that the base addresses are the same addresses used in the template C-code.
Should be no changes at this time.
2
3
1

## Slide 14: Verify Design
You should verify the addressing for all your design components before continuing.
Verify that the base addresses are the same addresses used in the template C-code.
Should be no changes at this time.

## Slide 15: Validate and Export Design
First click validate design_1
Regenerate the design_1 HDL wrapper.
Finally you need to generate the Generate Design bitstream
Take a coffee break while it builds

## Slide 16: SDK Project
Start with a “Hello World” project once in the SDK.
Rename the hello_world.c to Lec19.c and use the given Lec19.c code to get started
Modify the code to handle the interrupt generated from the counter and increment a counter variable for display.