## Slide 1: CSCE 436 – Advanced Embedded Systems Lecture 19 – Soft Core (MicroBlaze) + Custom IP
Prof Jeffrey Falkinburg Avery Hall 368 472-5120

## Slide 2: Lesson Outline
Time Logs!
MicroBlaze + Custom IP

## Slide 3: MicroBlaze + Custom IP

## Slide 4: MicroBlaze + Custom IP
axi_uartlite_0 @ 40600000
S_AXI_ACLK
S_AXI_ARESETN
slv_reg1
clk
reset_n
ctrl
Artix 7 (design_1)
MicroBlaze
Lec19.c
my_counter_ip_v1_0.vhd @ 0x44a00000
axi_lite
my_counter_ip_v1_0_S00_AXI.vhd
Lec19.vhd
32
slv_reg0
Q/D
32
Lec19.xdc
8
LED
T14
T15
T16
U16
V15
W16
W15
Y13
Design_1.xdc
AA19
V18
RX
RX
TX
TX
clk
reset_n
R4
G4
roll
slv_reg2

## Slide 5: MicroBlaze + Custom IP with Interrupt
axi_uartlite_0 @ 40600000
S_AXI_ACLK
S_AXI_ARESETN
slv_reg1
clk
reset_n
ctrl
Artix 7 (design_1)
MicroBlaze
my_counter_ip_v2_0.vhd @ 0x44a00000
my_counter_ip_v2_0_S00_AXI.vhd
Lec20.vhd
32
slv_reg0
Q/D
32
Lec19.xdc
8
LED
T14
T15
T16
U16
V15
W16
W15
Y13
Design_1.xdc
AA19
V18
RX
RX
TX
TX
clk
reset_n
R4
G4
roll
myISR()
main()
slv_reg2
Lec20.c
Interrupt
axi_lite
slv_reg3
flagQ
set
clear

## Slide 6: Lab 3
axi_uartlite_0 @ 40600000
S_AXI_ACLK
S_AXI_ARESETN
slv_reg1
clk
reset_n
ctrl
Artix 7 (design_1)
MicroBlaze
my_oscope_ip_v2_0.vhd @ 0x44a00000
my_oscope_ip_v2_0_S00_AXI.vhd
Lab3_dp.vhd
32
slv_reg0
Q/D
32
Lec19.xdc
8
LED
T14
T15
T16
U16
V15
W16
W15
Y13
Design_1.xdc
AA19
V18
RX
RX
TX
TX
clk
reset_n
R4
G4
roll
myISR()
main()
slv_reg2
Lab3.c
Interrupt
axi_lite
slv_reg3
flagQ
set
clear

## Slide 7: MicroBlaze + Custom IP

## Slide 8: MicroBlaze + Custom IP – Workflow
The work flow has three main steps.
  Define a new hardware design (MicroBlaze + axi_uartlite) in Vivado IP Integrator
  Create and package new custom IP (your custom hardware) and import it into your Vivado design
  Program the resulting hardware in the SDK environment.
Lets start with the first step.

## Slide 9: Xilinx Vivado – IP Integrator
  This step requires that you start a new hardware design (MicroBlaze + axi_uartlite) in Vivado IP Integrator in a new project called Lecture_19.
  You will add a new Block Design with a MicroBlaze and axi_uartlite following the MicroBlaze Tutorial.
https://reference.digilentinc.com/learn/programmable-logic/tutorials/nexys-video-getting-started-with-microblaze/start

## Slide 10: Xilinx Vivado – Create and Package Custom IP
  This step requires Create and package new custom IP (your custom hardware) and import it into your Vivado design.
  You will defined the logical arrangement of the component in VHDL. Your entity description will contain two types of connections; those targeted at external ports on the Artix 7 chip and those intended to be accessible to the MicroBlaze processor.
  You can also use this online tutorial to help guide you.
  https://reference.digilentinc.com/learn/programmable-logic/tutorials/zedboard-creating-custom-ip-cores/start

## Slide 11: Xilinx Vivado – Create and Package Custom IP
1. Open Vivado and create a new project
  Go to Tools→Create and package IP

## Slide 12: Xilinx Vivado – Create and Package Custom IP
2. Create your custom IP project
  2.1) Select Create a new AXI4 peripheral and click Next

## Slide 13: Xilinx Vivado – Create and Package Custom IP
  2.2) Input “My_Counter_IP” in the name field and click Next

## Slide 14: Xilinx Vivado – Create and Package Custom IP
  2.3) Change the number of Registers to 32 on the AXI interface and click Next

## Slide 15: Xilinx Vivado – Create and Package Custom IP
  2.4) Select Edit IP and click Finish

## Slide 16: Xilinx Vivado – Create and Package Custom IP
3. Designing the IP core
  3.1) A new instance of Vivado will open up for the new IP core. Expand the top level file My_Counter_IP_v1_0. Then double-click on My_Counter_IP_v1_0_S00_AXI to open it in the editor.

## Slide 17: Xilinx Vivado – Create and Package Custom IP
4. Adding the Lec 11 Counter to the My_Counter_IP_v1_0 project by adding the source lec19.vhd file
  Your counter will not yet be connected to the top level design

## Slide 18: Part 1a: Hardware Questions/ Notes related to handout
Note: the truth table for the counter is in the comments.
Q: In lec19.vhdl, what other library must be added?
Q: In lec19.vhdl, does the use work.lec19Parts.all library need to be added?

## Slide 19: MicroBlaze + Custom IP

## Slide 20: lec19.vhdl – Lec 11 Counter

## Slide 21: Part 1b: Hardware Questions/ Notes related to handout
Q: In my_counter_ip_v1_0_S00_AXI.vhd, what do the generics C_S_AXI_DATA_WIDTH do?
Q: In my_counter_ip_v1_0_S00_AXI.vhd, what two roles is slv_reg0 serving?
Q: In my_counter_ip_v1_0_S00_AXI.vhd, what roles does slv_reg1 serve?
Q: In my_counter_ip_v1_0_S00_AXI.vhd, slv_reg0 is on the left and right-hand side of an assignment. Identify the two lines where this happens.
Q: In my_counter_ip_v1_0_S00_AXI.vhd, on line 73, what is the role does X"000000" serve?

## Slide 22: MicroBlaze + Custom IP

## Slide 23: my_counter_ip_v1_0_S00_AXI.vhd – User Logic

## Slide 24: my_counter_ip_v1_0_S00_AXI.vhd – User Logic

## Slide 25: Xilinx Vivado – Create and Package Custom IP
5. Modifying My_Counter_IP_v1_0_S00_AXI axi bus interface file
  Add numeric standard library at the top of the file:
  use ieee.numeric_std.all;

## Slide 26: Xilinx Vivado – Create and Package Custom IP
5. Modifying My_Counter_IP_v1_0_S00_AXI axi bus interface file
  Add a port for the LEDs in the my_counter_ip_v1_0_S00_AXI entity between the comments:
  port (
  -- Users to add ports here
  LED : out std_logic_vector(7 downto 0);
  -- User ports ends
  -- Do not modify the ports beyond this line
  -- Global Clock Signal
  S_AXI_ACLK : in std_logic;

## Slide 27: Xilinx Vivado – Create and Package Custom IP
5. Modifying My_Counter_IP_v1_0_S00_AXI axi bus interface file
  Add the counter declaration and a signal for Q before begin in the my_counter_ip_v1_0_S00_AXI architecture:
  component lec11 is
  generic (N: integer := 4);
  Port( clk: in STD_LOGIC;
  reset_n : in STD_LOGIC;
  roll : out STD_LOGIC;
  ctrl: in std_logic_vector(1 downto 0);
  D: in unsigned (N-1 downto 0);
  Q: out unsigned (N-1 downto 0));
  end component;
  signal Q : unsigned (7 downto 0);

## Slide 28: Xilinx Vivado – Create and Package Custom IP
5. Modifying My_Counter_IP_v1_0_S00_AXI axi bus interface file
  Add the counter implementation and connect the wires within the my_counter_ip_v1_0_S00_AXI architecture:
  -- Add user logic here
  counter: lec11
  generic map (8)
  port map( clk => S_AXI_ACLK,
  reset_n => S_AXI_ARESETN,
  roll => roll_sig,
  ctrl => slv_reg1(1 downto 0),
  D => unsigned(slv_reg0(7 downto 0)),
  Q => Q);
  LED <= std_logic_vector(Q);

## Slide 29: Xilinx Vivado – Create and Package Custom IP
5. Modifying My_Counter_IP_v1_0_S00_AXI axi bus interface file
  Connect the counter implementation Q output signal to slave register 0 (slv_reg0) in the my_counter_ip_v1_0_S00_AXI architecture:
  loc_addr := axi_araddr(ADDR_LSB + OPT_MEM_ADDR_BITS downto ADDR_LSB); case loc_addr is
  when b"00000" =>
  reg_data_out <= x"000000" & std_logic_vector(Q);
  when b"00001" =>
  reg_data_out <= slv_reg1;
  when b"00010" =>
  reg_data_out <= slv_reg2;

## Slide 30: Part 1c: Hardware Questions/ Notes related to handout
Q: If you want a signal to go outside the Artix 7 chip...
  What files must it appear on the entity description?
  What other files must contain information about the signal?
Q: If you want a signal to go to the MicroBlaze...
  In order for the MicroBlaze to read the signal, what must you do?
  In order for the MicroBlaze to write to the signal, what must you do?

## Slide 31: MicroBlaze + Custom IP

## Slide 32: My_Counter_IP_v1_0.vhd – Top Level

## Slide 33: My_Counter_IP_v1_0.vhd – Top Level

## Slide 34: Xilinx Vivado – Create and Package Custom IP
6. Modifying My_Counter_IP_v1_0 top level file
  Add numeric standard library at the top of the file:
  use ieee.numeric_std.all;

## Slide 35: Xilinx Vivado – Create and Package Custom IP
6. Modifying My_Counter_IP_v1_0 top level file
  Add a port for the LEDs in the my_counter_ip_v1_0 entity between the comments to expose it to externally:
  port (
  -- Users to add ports here
  LED : out std_logic_vector(7 downto 0);
  -- User ports ends
  s00_axi_aclk : in std_logic;

## Slide 36: Xilinx Vivado – Create and Package Custom IP
6. Modifying My_Counter_IP_v1_0 top level file
  Add a port for the LEDs in the my_counter_ip_v1_0_S00_AXI component declaration:
  port (
  LED : out std_logic_vector(7 downto 0);
  S_AXI_ACLK : in std_logic;

## Slide 37: Xilinx Vivado – Create and Package Custom IP
6. Modifying My_Counter_IP_v1_0 top level file
  Add a port map for the LEDs in the my_counter_ip_v1_0_S00_AXI component instantiation:
  port map (
  LED => LED,
  S_AXI_ACLK => s00_axi_aclk,

## Slide 38: Xilinx Vivado – Create and Package Custom IP
7. Packaging the IP core
  Now that we have written the core, it is time to package up the HDL to create a complete IP package.
  7.1) Now click on Package IP in the Flow Navigator and you should see the Package IP tab. Select Compatibility and make sure “Artix7” are present. If those are not there, you can add them by clicking the plus button. The Life Cycle does not matter at this point.

## Slide 39: Xilinx Vivado – Create and Package Custom IP
7. Packaging the IP core

## Slide 40: Xilinx Vivado – Create and Package Custom IP
7.2) Select Customization Parameters and select the line for Merge Changes from Customization Parameters Wizard. This will have the My_Counter_IP parameters from the top file.

## Slide 41: Xilinx Vivado – Create and Package Custom IP
7.3) Select Customization GUI. This is were we get to change our graphical interface. No changes at this time.

## Slide 42: Xilinx Vivado – Create and Package Custom IP
7.4) Now the core should be complete so select Review and Package and click the Re-package IP button.

## Slide 43: Xilinx Vivado – Create and Package Custom IP
7.5) A popup will ask if you want to close the project, Select Yes.

## Slide 44: Xilinx Vivado – Create and Package Custom IP
8. Add Custom IP to your design
  8.1) In the project manager page of the original window, click Open Block Design. This adds a block design to the project.
  8.2) Use the Add IP button to add our Lec 11 Counter IP Core.

## Slide 45: Xilinx Vivado – Create and Package Custom IP
8. Add Custom IP to your design
  8.3) Right click on LEDs and select Make External and then run Connection Automation

## Slide 46: Xilinx Vivado – Create and Package Custom IP
8. Add Custom IP to your design
  8.4) The MIG block should read my_counter_ip_0. Place your cursor on this symbol || next to the LED[7:0] port name. Your cursor will change to look like a pencil. Right click here and in the drop down list select Make External or left click on || and use the keyboard shortcut, “Ctrl+t”.

## Slide 47: Xilinx Vivado – Create and Package Custom IP
8. Add Custom IP to your design
  8.5) Your custom IP should now be connected. Now you need to add a constraints file to add the LED net to the pins on the Artix 7 chip by adding the following lines to the lec19.xdc file.
  ## LEDs
  set_property -dict { PACKAGE_PIN T14 IOSTANDARD LVCMOS25 } [get_ports { LED[0] }]; #IO_L15P_T2_DQS_13 Sch=led[0]
  set_property -dict { PACKAGE_PIN T15 IOSTANDARD LVCMOS25 } [get_ports { LED[1] }]; #IO_L15N_T2_DQS_13 Sch=led[1]
  set_property -dict { PACKAGE_PIN T16 IOSTANDARD LVCMOS25 } [get_ports { LED[2] }]; #IO_L17P_T2_13 Sch=led[2]
  set_property -dict { PACKAGE_PIN U16 IOSTANDARD LVCMOS25 } [get_ports { LED[3] }]; #IO_L17N_T2_13 Sch=led[3]
  set_property -dict { PACKAGE_PIN V15 IOSTANDARD LVCMOS25 } [get_ports { LED[4] }]; #IO_L14N_T2_SRCC_13 Sch=led[4]
  set_property -dict { PACKAGE_PIN W16 IOSTANDARD LVCMOS25 } [get_ports { LED[5] }]; #IO_L16N_T2_13 Sch=led[5]
  set_property -dict { PACKAGE_PIN W15 IOSTANDARD LVCMOS25 } [get_ports { LED[6] }]; #IO_L16P_T2_13 Sch=led[6]
  set_property -dict { PACKAGE_PIN Y13 IOSTANDARD LVCMOS25 } [get_ports { LED[7] }]; #IO_L5P_T0_13 Sch=led[7]

## Slide 48: MicroBlaze + Custom IP

## Slide 49: Updating Custom IP
Right click on custom IP and click Edit in IP Packager if you want to modify! Otherwise skip to validate design.
1
2
9
9

## Slide 50: Xilinx Vivado – Create and Package Custom IP
Now that you updated the core you need to re-select Review and Package and click the Re-package IP button.

## Slide 51: Updating Custom IP
Refresh IP Catalog, Upgrade IP and then Re-Generate
1
2

## Slide 52: Verify Design
You should verify the addressing for all your design components before continuing.
Verify that the base addresses are the same addresses used in the template C-code.
Should be no changes at this time.
2
3
1

## Slide 53: Validate and Export Design
First click validate design_1
Regenerate the design_1 HDL wrapper.
Finally you need to generate the Generate Design bitstream
Take a coffee break while it builds

## Slide 54: Export Design
Exporting Hardware Design to SDK…be sure to include the bitstream…assuming no errors

## Slide 55: Launch SDK
Go to File and select Launch SDK and click OK.

## Slide 56: New SDK Project
9
9

## Slide 57: New SDK Project
Need to do the Hello World template so it generates the platform header files!

## Slide 58: New C Source File

## Slide 59: New C Source File
9

## Slide 60: Lec19.c

## Slide 61: Lec19.c

## Slide 62: Lec19.c

## Slide 63: Lec19.c

## Slide 64: Lec19.c

## Slide 65: Lec19.c

## Slide 66: Part 2: Software Questions/ Notes related to handout
Why doesn't the 'c' command cause the counter to count up by 1?
On line 130, why did I subtract 0x30?
After loading the counter on line 132, something should be done that is missing.
What line of VHDL code in my_counter_ip_v1_0_S00_AXI.vhd is "activated" when line 80 executes?
What line of VHDL code in my_counter_ip_v1_0_S00_AXI.vhd is "activated" when line 141 executes?
What line of VHDL code in lec19.vhdl "activated" when line 141 executes?
What appears to be the naming convention for hardware registers?

## Slide 67: Add C code to Source File

## Slide 68: Xilinx Software Development Kit - SDK
In the SDK environment, you program the hardware built in the previous step.
The key concept here is that the peripheral defined in Vivado design are accessible through the slave registers as memory mapped devices.
Verify your my_counter_ip_v1_0 Base Address in system.hdf file is assigned to be 0x44a00000.
In the my_counter_ip_v1_0_S00_AXI.vhdl file, I (arbitrarily) assigned counter ports to slave register according to the table below.
Signal | direction | Slave Register | Address
D | Input | slv_reg0(7 downto 0) | 0x44a00000
ctrl | Input | slv_reg1(1 downto 0) | 0x44a00004
Q | Output | slv_reg0(7 downto 0) | 0x44a00000

## Slide 69: Increase Stack and Heap Size
You may have to add more Stack and Heap to your design
9
9
1
2
3

## Slide 70: Build and Export to FPGA

## Slide 71: Run Configuration
Run Configuration Settings for STDIO Connection
  After the FPGA has been successfully programmed with the bit file, from the Project Explorer panel, right click on the display_hello_world project folder which has been highlighted in the screen capture below. At the bottom of the drop down list, select Run As and then select Run Configurations.
The Run Configurations window is divided into two main sections. In the left panel, under Xilinx C/C++ application(GDB), select Lec19.elf. Note: In case you see display_hello_world Debug instead of display_hello_world.elf in this step, you can still run it without any issues. On the right side of this window, you will see five main tabs. Select the STDIO Connection tab.

## Slide 72: COM Port Selection for STDIO connection

## Slide 73: Run Configuration

## Slide 74: MicroBlaze + Custom IP