## Slide 1: CSCE 436 – Advanced Embedded Systems Lecture 3 – Combinational Element, unsigned, constraints file, synthesis
Prof Jeffrey Falkinburg Avery Hall 368 472-5120

## Slide 2: Lesson Outline
Time Logs!
HW #2 Due Now!
Synthesis
Constraints file
Combinational Element
Unsigned Numeric Standard
Combinations

## Slide 3
https://www.xilinx.com/support/documentation/user_guides/ug475_7Series_Pkg_Pinout.pdf
pp 80

## Slide 4: Synthesis

## Slide 5: Synthesis
Insert this code into your Majority.xdc file
  Inputs from switches and outputs to LEDs
# This is slide switch SW0
set_property -dict { PACKAGE_PIN E22 IOSTANDARD LVCMOS12 } [get_ports { a }]; #IO_L22P_T3_16 Sch=sw[0]
# This is slide switch SW1
set_property -dict { PACKAGE_PIN F21 IOSTANDARD LVCMOS12 } [get_ports { b }]; #IO_25_16 Sch=sw[1]
# This is slide switch SW2
set_property -dict { PACKAGE_PIN G21 IOSTANDARD LVCMOS12 } [get_ports { c }]; #IO_L24P_T3_16 Sch=sw[2]
# This is LED Led(0)
set_property -dict { PACKAGE_PIN T14 IOSTANDARD LVCMOS25 } [get_ports { f }]; #IO_L15P_T2_DQS_13 Sch=led[0]
UUT: Majority
a
b
c
f
Xilix Chip
E22
F21
G21
T14

## Slide 6: Constraints file

## Slide 7: Constraints file
Nexyx Video Master XDC
  https://cse.unl.edu/~jfalkinburg/cse_courses/2022/436/datasheets/NexysVideo_Master.xdc

## Slide 8: Combinational Element

## Slide 9: Combinational Element – Common error
Common error that may come up in your designs
You cannot use a variable listed on the entity as an out port, on the right hand side of a signal assignment statement.
  entity circuit is
  port (clk, data: in std_logic;
  q, not_q: out std_logic);
  end circuit;
  architecture error of circuit is
  begin
  q <= some cool logical stuff using clk and data;
  not_q <= not q;
  end error;

## Slide 10: Combinational Element – Solution
Solution
assign "some cool logical stuff using clk and data" to a temporary variable
  entity circuit is
  port (clk, data: in std_logic;
  q, not_q: out std_logic);
  end circuit;
  architecture error of circuit is
  signal temp std_logic;
  begin
  temp <= some cool logical stuf using clk and data;
  q <= temp;
  not_q <= not temp;
  end error;

## Slide 11: Combinational Element - Mux
Simplify muxes using conditional signal assignment statement
Example:
  x <= y0 when S = "00" else
  y1 when S = "01" else
  y2 when S = "10" else
  y3;
Draw this Circuit assuming 8-bit inputs
Now build 4-1 mux w/ 2-1 muxes

## Slide 12: Unsigned Numeric Standard

## Slide 13: Unsigned Numeric Standard
So far we mostly used STD_LOGIC_1164 library
  library IEEE;
  use IEEE.STD_LOGIC_1164.all;
  Library Contents: http://www.csee.umbc.edu/portal/help/VHDL/packages/std_logic_1164.vhd

## Slide 14: Unsigned Numeric Standard
Numeric_Std Library supports 2 main datatypes
  Signed and Unsigned
  Library Contents: http://www.csee.umbc.edu/portal/help/VHDL/packages/numeric_std.vhd
  library IEEE;
  use IEEE.std_logic_1164.all;
  use IEEE.NUMERIC_STD.ALL;
  entity lec3 is
  port( au, bu: in unsigned(3 downto 0);
  cu,du,su: out unsigned(3 downto 0);
  as, bs: in signed(3 downto 0);
  cs,ds,ss: out signed(3 downto 0));
  end lec3;

## Slide 15: Unsigned Numeric Standard
  architecture structure of lec3 is
  begin
  cu <= "1000" when (au > bu) else
  "0110" when (au = bu) else
  "0001";
  su <= au + bu;
  du <= au - bu;
  cs <= "1000" when (as > bs) else
  "0110" when (as = bs) else
  "0001";
  ss <= as + bs;
  ds <= as - bs;

## Slide 16: Unsigned Numeric Standard
Unsigned
Signed
A | B | Value A | Value B | A >? B | A =? B | A <? B | A + B | A - B
0010 | 0100 |  |  |  |  |  |  | 
1011 | 0001 |  |  |  |  |  |  | 
0110 | 1010 |  |  |  |  |  |  | 
0111 | 1000 |  |  |  |  |  |  | 
A | B | Value A | Value B | A >? B | A =? B | A <? B | A + B | A - B
0010 | 0100 |  |  |  |  |  |  | 
1011 | 0001 |  |  |  |  |  |  | 
0110 | 1010 |  |  |  |  |  |  | 
0111 | 1000 |  |  |  |  |  |  | 

## Slide 17: Unsigned Numeric Standard

## Slide 18: Unsigned Numeric Standard
You will typically use STD_LOGIC_VECTOR and UNSIGNED
You may need to convert between the two
  a: std_logic_vector(7 downto 0);
  b: unsigned(7 downto 0);
  c: std_logic_vector(7 downto 0);
  b <= unsigned(a);
  c <= std_logic_vector(b);

## Slide 19: Using Unsigned and Decimal Numbers
Convert Decimal number to Unsigned Vector (7 downto 0)
  to_unsigned(17, 8)
  First argument is the decimal number
  Second argument is the number of bits
Conditional with unsigned number
  LED_Trigger <= '1' when (Binary_Input = to_unsigned(17, 8) ) else
  ‘0';

## Slide 20: Combinations

## Slide 21: Combinations
Common Combinations if/then/else
All conditional statements consist of three parts:
  the condition to be checked (the if clause)
  the statement to be evaluated when the condition is true (the then clause)
  the statement to be evaluated when the condition is false (the else clause)
Typically, the condition being evaluated seeks the relative magnitude of two unsigned binary numbers, requiring a comparator.
The then and else clauses will typically require some logic or arithmetic operation

## Slide 22: Combinations
In order to illustrate the hardware realization of a conditional statement, consider the following example:
  C: if (a<4) then z=y+3 else z=y+7
  VHDL: z <= y+3 when (a < 4) else y+7;

## Slide 23: Combinations
However, this circuit is not minimal, one of the adders can be removed.
How?
Practice on Homework

## Slide 24: Lesson Outline
Synthesis
Constraints file
Combinational Element
Unsigned Numeric Standard
Combinations