## Slide 1: CSCE 436 – Advanced Embedded Systems Lecture 27 – Digital Low Pass Filter
Prof Jeffrey Falkinburg Avery Hall 368 472-5120

## Slide 2: Lesson Outline
Time Logs!
Project Proposals Due Today
Digital Low Pass Filter
  Filtering
  Low Pass Filter
  Filter Design Problems

## Slide 3: Filtering

## Slide 4: Filtering
Problem with sampling analog signal at discrete times?
  Aliasing problems with frequency folding

## Slide 5: Filtering
Frequency Folding creates problems in sampled systems like an ADC because noise anywhere in the spectrum will fold back into our sampling region as shown below
Notes: Observed frequency chart shows amplitude vs frequency.

## Slide 6: Filtering
In order to address this problem we will utilize a principle called attenuation.
Attenuation - process of changing the amplitude of a waveform without changing its frequency.
Amount of attenuation is quantified in terms of decibels.
dB = 20 * log (V_out/V_in)
V_out/Vin | dB
1 | 0
1/10 | -20
1/100 | -40
1/1000 | -60
1/256 | -48.1648
1/1024 | -60.206
1/1.41254 | -3dB
1/2512 | -68dB
0.1V
48KHz

## Slide 7: Filtering Questions

## Slide 8: Filtering Questions
Question 1: If you input a 1v sin wave into a circuit that attenuated it by -40dB, what would the amplitude of the output waveform be?
Given: dB = 20 * log (V_out/V_in)
  -40db = 20 log (V_out/1V_in)
  -2 = log (V_out/1V_in)
  V_out = 10-2
  V_out = 0.01
  V_out = 10mV

## Slide 9: Filtering Questions
Question 2: If you input a 1v sin wave into a circuit that attenuated it by -68dB, what would the amplitude of the output waveform be?
Given: dB = 20 * log (V_out/V_in)
  -68db = 20 log (V_out/1V_in)
  -3.4 = log (V_out/1V_in)
  V_out = 10-3.4
  V_out = 0.4mV

## Slide 10: Filtering Questions
Question 3: If you reduced a signal by a factor of 1/256, how many dB would you need to attenuate it by?
Given: dB = 20 * log (V_out/V_in)
  dB = 20 log (1/256)
  dB = -48dB

## Slide 11: Low Pass Filter

## Slide 12: Low Pass Filter
We will use a circuit called a low pass filter to attenuate signals.
  You can build an analog low pass filter by putting a resistor and capacitor in parallel.

## Slide 13: Low Pass Filter
Low Pass Filter
Passive Low Pass Filter:
https://www.electronics-tutorials.ws/filter/filter_2.html
Vin
Vout

## Slide 14: Low Pass Filter
The Atlys boards had this circuit arrangement as shown by the pairs (R153, C43) and (R154,C44) in the schematic below.
Strategic parameters for this first order filter include...
  Corner frequency: 72KHz
  Roll off: -20dB/decade

## Slide 15: Low Pass Filter
For a Low Pass filter, the attenuation applied to an input signal depends on the input frequency.
Relationship is characterized in the filters frequency response graph. http://www.electronics-tutorials.ws/filter/fil10.gif

## Slide 16: Nexyx Video Audio Codec Schematic

## Slide 17: High Pass Filter
Our Nexys Video boards have this circuit arrangement as shown by the pairs (R111, C49) and (R112,C50) in the schematic below.
Strategic parameters for this first order High Pass filter include...
  Corner frequency: 1.59 Hz
  Roll off: -20dB/decade

## Slide 18: Filter Design Problems

## Slide 19: Filter Design Problem
Lets test out understanding of all these concepts with a filter design problem.
1. Aliasing:
Your sampling an analog signal at 48KHz. List all the frequencies that will look like 2KHz signals.
  1st harmonic: 2KHz
  48KHz-2KHz = 46KHz
  2nd harmonic: 48KHz+2KHz=50KHz
  96KHz-2KHz = 94KHz
  3rd harmonic: 96KHz+2KHz=98KHz 144KHz-2KHz = 142KHz

## Slide 20: Filter Design Problem
2. Decades:
A first-order LPF has a cutoff frequency of 2KHz. Describe the attenuation of a 80KHz input signal in decibels and as a ratio of output voltage to input voltage.
  Since a decade is a multiplicative factor of 10, we need to find how may powers of 10 you have to multiply by in order to increase 2 to 80. In other words
  2*10^x = 80, solving for X yields
  x = log_10(80/2) = 1.6 Decades

## Slide 21: Filter Design Problem
2. Decades:
  1 KHz  10 KHz  1 Decades
  10 KHz  100 KHz  1 Decades
  1 KHz  100 KHz  2 Decades
  1 KHz  48 KHz  1.7 Decades

## Slide 22: Filter Design Problem
2. Decades Cont:
  So we know that a 80KHz waveform is 1.6 decades above a 2KHz waveform. Since the LPF attenuates -20db/decade, the 80Kkz waveform will be attenuated 1.6*-20 = -32db
  Decibels can be converted to the ratio of output/input using its definition...
  -32db = 20db log_10(V_out/V_in)
  V_out/Vin = 0.025 = 1/40

## Slide 23: Filter Design Problem
3. ADC convert:
You are working with a 10-bit ADC and would like to attenuate some frequency below 1/2 ULP. How many dB will be required to achieve this?
  A 10-bit ADC has a range of [0-1023], so half the unit of least place will be 1 part in 2048
  In terms of decibels this is
  20*log_10(1/2^11) = -66dB
ADC convert Cont:
What if we change it to 1 ULP?
  20*log(2-10)= 60dB

## Slide 24: Filter Design Problem
4. Sampling frequency:
Given:
  Signal of interest is 0-2KHz
  2nd order filter
  10-bit ADC
What is the minimum sampling rate at 1 ULP?
  Reduce first fold-back to -60bB so that its at most 1ULP. Since the corner frequency is set to 2KHz, first fold-back to 2KHz must be reduced by -57dB.
  At -40dB/decade this is 1.425 decades above 2KHz
  Fs-2KHz = 2KHz*10^1.425 = 53KHz.
  Thus, the minimum sampling frequency Fs=55KHz.

## Slide 25: Filter Design Problem
4. Sampling frequency:
Given:
  Signal of interest is 0-2KHz
  2nd order filter
  10-bit ADC
What is the minimum sampling rate at 0.5 ULP?
  Reduce first fold-back to -66bB so that its at most 1/2ULP. Since the corner frequency is set to 2KHz, first fold-back to 2KHz must be reduced by -63dB.
  At -40dB/decade this is 1.58 decades above 2KHz
  Fs-2KHz = 2KHz*10^1.58 = 76KHz.
  Thus, the minimum sampling frequency is 78KHz.

## Slide 26: Filter Design Problem
5. Sampling frequency:
Given:
  Signal of interest is 0-2KHz
  1st order filter
  8-bit ADC
What is the sampling rate?
  The underlying goal here is to reduce any noise folded back into our signal band below 1 ULP in the ADC.
  Since we are using an 8-bit ADC, we want to reduce the noise to 1/256 (i.e. 1/2^8) of the signal.
  This works out to -48dB (i.e. 20*log_10(2^-8))

## Slide 27: Filter Design Problem
5. Sampling frequency Cont:
  If we sample the signal at F_s, then the region between [F_s-2k, F_s] will get folded back into our signal band.
  Consequently, the filter must be between 2k and F_s-2k to attenuate the signal.
  Since we have a first order filter, we will get -20dB of attenuation for every decade.
  Since we need -48dB, we will need 2.4 decades, or a factor of 251 over 2k or 502KHz.
  F_s - 2K = 2K * 10^2.4 = 502.38KHz
  Thus we have F_s - 2k = 502k or F_s = 504KHz.
Notes: 2.4 decades  (-20dB/decade = -48 dB/x decades)
factor of 251  (10^2.4 = 251)
F_s - 2K = 2K * 10^2.4 = 502.38KHz

## Slide 28: Filter Design Problem
6. Sampling frequency:
Given:
  Signal of interest is 0-2KHz
  1st order filter
  10-bit ADC
What is the minimum sampling rate at 1/2ULP?
  Reduce first fold-back to -66bB so that its at most 1/2ULP. Since the corner frequency is set to 2Kh, first fold-back to 2KHz must be reduced -63dB. At -20dB/decade this is 3.15 decades above 2KHz or 2KHz*10^3.15 = 2.8Mhz
  Thus, the minimum sampling frequency is Fs = 2.8Mhz + 2KHz = 2.8Mhz
  Wow, what a difference that extra order in the filter made!

## Slide 29: Filter Design Problem
7. Filter specs:
Given:
  Signal of interest is 0-2KHz
  8-bit ADC
  Maximum possible sampling rate of 80KHz
What order filter do we need?
  An 8-bit ADC required -48db of attenuation to get the noise below 1ulp (unit of least place). From 2KHz to 78KHz is 1.6 decades (solve 2K*10^x = 78K)
  The roll off of an x-order LPF is -20*x db/decade.
-20*x db -48 db
------------ = ---------------  x = 1.5, so 2nd order filter is needed.
decade 1.6 decade

## Slide 30: Filter Design Problem
8. Signal bandwidth:
Given:
  16-bit ADC
  4th order filter
  Sampling frequency 250KHz
What is the maximum frequency of the signal of interest?
  A 16-bit ADC required -96db of attenuation to get the noise below 1ulp.
  Let the sampling frequency be called Falpha.
  Fold back will occur at 250k - Falpha.

## Slide 31: Filter Design Problem

## Slide 32: Filter Design Problem
8. Signal bandwidth Cont:
  Filter must attenuate signal over:
  Falpha*10^x = 250k - Falpha
  log((250k - Falpha) / Falpha) decades
  4th order filter rolls off at -80db/decade
  -80 db -96 db
  -------- = ------------------------------
  decade log((250k - Falpha)/Falpha) decade
  Falpha= 14.8KHz