## Slide 1: CSCE 436 – Advanced Embedded Systems Lecture 19 – Soft Core (MicroBlaze) + Custom IP
Prof Jeffrey Falkinburg Avery Hall 368 472-5120

## Slide 2: Lesson Outline
MicroBlaze + Custom IP

## Slide 3: MicroBlaze + Custom IP

## Slide 4: MicroBlaze + Custom IP
axi_uartlite_0 @ 40600000
S_AXI_ACLK
S_AXI_ARESETN
slv_reg1
clk
reset_n
ctrl
Artix 7 (design_1)
MicroBlaze
Lec19.c
my_counter_ip_v1_0.vhd @ 0x44a00000
axi_lite
my_counter_ip_v1_0_S00_AXI.vhd
Lec19.vhd
32
slv_reg0
Q/D
32
Lec19.xdc
8
LED
T14
T15
T16
U16
V15
W16
W15
Y13
Design_1.xdc
AA19
V18
RX
RX
TX
TX
clk
reset_n
R4
G4
roll
slv_reg2

## Slide 5: MicroBlaze + Custom IP with Interrupt
axi_uartlite_0 @ 40600000
S_AXI_ACLK
S_AXI_ARESETN
slv_reg1
clk
reset_n
ctrl
Artix 7 (design_1)
MicroBlaze
my_counter_ip_v2_0.vhd @ 0x44a00000
my_counter_ip_v2_0_S00_AXI.vhd
Lec20.vhd
32
slv_reg0
Q/D
32
Lec19.xdc
8
LED
T14
T15
T16
U16
V15
W16
W15
Y13
Design_1.xdc
AA19
V18
RX
RX
TX
TX
clk
reset_n
R4
G4
roll
myISR()
main()
slv_reg2
Lec20.c
Interrupt
axi_lite
slv_reg3
flagQ
set
clear

## Slide 6: Lab 3
axi_uartlite_0 @ 40600000
S_AXI_ACLK
S_AXI_ARESETN
slv_reg1
clk
reset_n
ctrl
Artix 7 (design_1)
MicroBlaze
my_oscope_ip_v2_0.vhd @ 0x44a00000
my_oscope_ip_v2_0_S00_AXI.vhd
Lab3_dp.vhd
32
slv_reg0
Q/D
32
Lec19.xdc
8
LED
T14
T15
T16
U16
V15
W16
W15
Y13
Design_1.xdc
AA19
V18
RX
RX
TX
TX
clk
reset_n
R4
G4
roll
myISR()
main()
slv_reg2
Lab3.c
Interrupt
axi_lite
slv_reg3
flagQ
set
clear

## Slide 7: MicroBlaze + Custom IP

## Slide 8: MicroBlaze + Custom IP – Workflow
The work flow has three main steps.
  Define a new hardware design (MicroBlaze + axi_uartlite) in Vivado IP Integrator
  Create and package new custom IP (your custom hardware) and import it into your Vivado design
  Program the resulting hardware in the SDK/Vitis environment.
Lets start with the first step.

## Slide 9: Xilinx Vivado – IP Integrator
  This step requires that you start a new hardware design (MicroBlaze + axi_uartlite) in Vivado IP Integrator in a new project called Lecture_19.
  You will add a new Block Design with a MicroBlaze and axi_uartlite following the MicroBlaze Tutorial.
https://digilent.com/reference/programmable-logic/guides/getting-started-with-ipi (New Tutorial for Vitis)
https://reference.digilentinc.com/learn/programmable-logic/tutorials/nexys-video-getting-started-with-microblaze/start (Old Tutorial for SDK)

## Slide 10: Xilinx Vivado – Create and Package Custom IP
  This step requires Create and package new custom IP (your custom hardware) and import it into your Vivado design.
  You will defined the logical arrangement of the component in VHDL. Your entity description will contain two types of connections; those targeted at external ports on the Artix 7 chip and those intended to be accessible to the MicroBlaze processor.
  You can also use this online tutorial to help guide you.
  https://reference.digilentinc.com/learn/programmable-logic/tutorials/zedboard-creating-custom-ip-cores/start

## Slide 11: Xilinx Vivado – Create and Package Custom IP
1. Open Vivado and create a new project
  Go to Tools→Create and package IP

## Slide 12: Xilinx Vivado – Create and Package Custom IP
2. Create your custom IP project
  2.1) Select Create a new AXI4 peripheral and click Next

## Slide 13: Xilinx Vivado – Create and Package Custom IP
  2.2) Input “My_Counter_IP” in the name field and click Next

## Slide 14: Xilinx Vivado – Create and Package Custom IP
  2.3) Change the number of Registers to 32 on the AXI interface and click Next

## Slide 15: Xilinx Vivado – Create and Package Custom IP
  2.4) Select Edit IP and click Finish

## Slide 16: Xilinx Vivado – Create and Package Custom IP
3. Designing the IP core
  3.1) A new instance of Vivado will open up for the new IP core. Expand the top level file My_Counter_IP_v1_0. Then double-click on My_Counter_IP_v1_0_S00_AXI to open it in the editor.

## Slide 17: Xilinx Vivado – Create and Package Custom IP
Error opening My_Counter_IP_v1_0 in editor. Vivado getting stuck initializing language server:
  Change the option "Tools -> Settings -> Tool Settings -> Text Editor -> Syntax Checking -> Syntax checking" from Sigasi to Vivado, then restart Vivado.

## Slide 18: Xilinx Vivado – Create and Package Custom IP
4. Adding the Lec 11 Counter to the My_Counter_IP_v1_0 project by adding the source lec19.vhd file
  Your counter will not yet be connected to the top level design

## Slide 19: Part 1a: Hardware Questions/ Notes related to handout
Note: the truth table for the counter is in the comments.
Q: In lec19.vhdl, what other library must be added?
Q: In lec19.vhdl, does the use work.lec19Parts.all library need to be added?

## Slide 20: MicroBlaze + Custom IP

## Slide 21: lec19.vhdl – Lec 11 Counter
unsigned (N-1 downto 0)
(others => '0')
processQ + 1
unsigned(D)
(others => '0')

## Slide 22: Part 1b: Hardware Questions/ Notes related to handout
Q: In my_counter_ip_v1_0_S00_AXI.vhd, what do the generics C_S_AXI_DATA_WIDTH do?
Q: In my_counter_ip_v1_0_S00_AXI.vhd, what two roles is slv_reg0 serving?
Q: In my_counter_ip_v1_0_S00_AXI.vhd, what roles does slv_reg1 serve?
Q: In my_counter_ip_v1_0_S00_AXI.vhd, slv_reg0 is on the left and right-hand side of an assignment. Identify the two lines where this happens.
Q: In my_counter_ip_v1_0_S00_AXI.vhd, on line 73, what is the role does X"000000" serve?

## Slide 23: MicroBlaze + Custom IP

## Slide 24: my_counter_ip_v1_0_S00_AXI.vhd – User Logic
Q

## Slide 25: my_counter_ip_v1_0_S00_AXI.vhd – User Logic
lec11
8
S_AXI_ACLK
S_AXI_ARESETN
Q

## Slide 26: Xilinx Vivado – Create and Package Custom IP
5. Modifying My_Counter_IP_v1_0_S00_AXI axi bus interface file
  Add numeric standard library at the top of the file:
  use ieee.numeric_std.all;

## Slide 27: Xilinx Vivado – Create and Package Custom IP
5. Modifying My_Counter_IP_v1_0_S00_AXI axi bus interface file
  Add a port for the LEDs in the my_counter_ip_v1_0_S00_AXI entity between the comments:
  port (
  -- Users to add ports here
  LED : out std_logic_vector(7 downto 0);
  -- User ports ends
  -- Do not modify the ports beyond this line
  -- Global Clock Signal
  S_AXI_ACLK : in std_logic;

## Slide 28: Xilinx Vivado – Create and Package Custom IP
5. Modifying My_Counter_IP_v1_0_S00_AXI axi bus interface file
  Add the counter declaration and a signal for Q before begin in the my_counter_ip_v1_0_S00_AXI architecture:
  component lec11 is
  generic (N: integer := 4);
  Port( clk: in STD_LOGIC;
  reset_n : in STD_LOGIC;
  --roll : out STD_LOGIC; --don’t add this yet
  ctrl: in std_logic_vector(1 downto 0);
  D: in unsigned (N-1 downto 0);
  Q: out unsigned (N-1 downto 0));
  end component;
  signal Q : unsigned (7 downto 0);

## Slide 29: Xilinx Vivado – Create and Package Custom IP
5. Modifying My_Counter_IP_v1_0_S00_AXI axi bus interface file
  Add the counter implementation and connect the wires within the my_counter_ip_v1_0_S00_AXI architecture:
  -- Add user logic here
  counter: lec11
  generic map (8)
  port map( clk => S_AXI_ACLK,
  reset_n => S_AXI_ARESETN,
  --roll => roll_sig, --don’t add this yet
  ctrl => slv_reg1(1 downto 0),
  D => unsigned(slv_reg0(7 downto 0)),
  Q => Q);
  LED <= std_logic_vector(Q);

## Slide 30: Xilinx Vivado – Create and Package Custom IP
5. Modifying My_Counter_IP_v1_0_S00_AXI axi bus interface file
  Connect the counter implementation Q output signal to slave register 0 (slv_reg0) in the my_counter_ip_v1_0_S00_AXI architecture:
  loc_addr := axi_araddr(ADDR_LSB + OPT_MEM_ADDR_BITS downto ADDR_LSB); case loc_addr is
  when b"00000" =>
  reg_data_out <= x"000000" & std_logic_vector(Q);
  when b"00001" =>
  reg_data_out <= slv_reg1;
  when b"00010" =>
  reg_data_out <= slv_reg2;

## Slide 31: Part 1c: Hardware Questions/ Notes related to handout
Q: If you want a signal to go outside the Artix 7 chip...
  What files must it appear on the entity description?
  What other files must contain information about the signal?
Q: If you want a signal to go to the MicroBlaze...
  In order for the MicroBlaze to read the signal, what must you do?
  In order for the MicroBlaze to write to the signal, what must you do?

## Slide 32: MicroBlaze + Custom IP

## Slide 33: My_Counter_IP_v1_0.vhd – Top Level

## Slide 34: My_Counter_IP_v1_0.vhd – Top Level

## Slide 35: Xilinx Vivado – Create and Package Custom IP
6. Modifying My_Counter_IP_v1_0 top level file
  Add numeric standard library at the top of the file:
  use ieee.numeric_std.all;

## Slide 36: Xilinx Vivado – Create and Package Custom IP
6. Modifying My_Counter_IP_v1_0 top level file
  Add a port for the LEDs in the my_counter_ip_v1_0 entity between the comments to expose it to externally:
  port (
  -- Users to add ports here
  LED : out std_logic_vector(7 downto 0);
  -- User ports ends
  s00_axi_aclk : in std_logic;

## Slide 37: Xilinx Vivado – Create and Package Custom IP
6. Modifying My_Counter_IP_v1_0 top level file
  Add a port for the LEDs in the my_counter_ip_v1_0_S00_AXI component declaration:
  port (
  LED : out std_logic_vector(7 downto 0);
  S_AXI_ACLK : in std_logic;

## Slide 38: Xilinx Vivado – Create and Package Custom IP
6. Modifying My_Counter_IP_v1_0 top level file
  Add a port map for the LEDs in the my_counter_ip_v1_0_S00_AXI component instantiation:
  port map (
  LED => LED,
  S_AXI_ACLK => s00_axi_aclk,

## Slide 39: Xilinx Vivado – Create and Package Custom IP
7. Packaging the IP core
  Now that we have written the core, it is time to package up the HDL to create a complete IP package.
  7.1) Now click on Package IP in the Flow Navigator and you should see the Package IP tab. Select Compatibility and make sure “Artix7” are present. If those are not there, you can add them by clicking the plus button. The Life Cycle does not matter at this point.

## Slide 40: Xilinx Vivado – Create and Package Custom IP
7. Packaging the IP core

## Slide 41: Xilinx Vivado – Create and Package Custom IP
7.2) Select Customization Parameters and select the line for Merge Changes from Customization Parameters Wizard. This will have the My_Counter_IP parameters from the top file.

## Slide 42: Xilinx Vivado – Create and Package Custom IP
7.3) Select Customization GUI. This is were we get to change our graphical interface. No changes at this time.

## Slide 43: Xilinx Vivado – Create and Package Custom IP
7.4) Now the core should be complete so select Review and Package and click the Re-package IP button.

## Slide 44: Xilinx Vivado – Create and Package Custom IP
7.5) A popup will ask if you want to close the project, Select Yes.

## Slide 45: Xilinx Vivado – Create and Package Custom IP
  Before you add your Custom IP to your design update the Makefile in the ip_repo/my_counter_ip_1.0/drivers folder using the following code (Fixing this now will eliminate issues later in Vitis):
COMPILER=
ARCHIVER=
CP=cp
COMPILER_FLAGS=
EXTRA_COMPILER_FLAGS=
LIB=libxil.a
RELEASEDIR=../../../lib
INCLUDEDIR=../../../include
INCLUDES=-I./. -I${INCLUDEDIR}
INCLUDEFILES=*.h
LIBSOURCES=$(wildcard *.c)
OBJECTS = $(addsuffix .o, $(basename $(wildcard *.c)))
ASSEMBLY_OBJECTS = $(addsuffix .o, $(basename $(wildcard *.S)))
libs:
echo "Compiling simple_adder..."
$(COMPILER) $(COMPILER_FLAGS) $(EXTRA_COMPILER_FLAGS) $(INCLUDES) $(LIBSOURCES)
$(ARCHIVER) -r ${RELEASEDIR}/${LIB} ${OBJECTS} ${ASSEMBLY_OBJECTS}
make clean
include:
${CP} $(INCLUDEFILES) $(INCLUDEDIR)
clean:
rm -rf ${OBJECTS} ${ASSEMBLY_OBJECTS}

## Slide 46: Xilinx Vivado – Create and Package Custom IP
8. Add Custom IP to your design
  8.1) In the project manager page of the original window, click Open Block Design. This adds a block design to the project.
  8.2) Use the Add IP button to add our Lec 11 Counter IP Core.

## Slide 47: Xilinx Vivado – Create and Package Custom IP
8. Add Custom IP to your design
  8.3) Right click on LEDs and select Make External and then run Connection Automation

## Slide 48: Xilinx Vivado – Create and Package Custom IP
8. Add Custom IP to your design
  8.4) The MIG block should read my_counter_ip_0. Place your cursor on this symbol || next to the LED[7:0] port name. Your cursor will change to look like a pencil. Right click here and in the drop down list select Make External or left click on || and use the keyboard shortcut, “Ctrl+t”.

## Slide 49: Xilinx Vivado – Create and Package Custom IP
8. Add Custom IP to your design
  8.5) Your custom IP should now be connected. Now you need to add a constraints file to add the LED net to the pins on the Artix 7 chip by adding the following lines to the lec19.xdc file.
  ## LEDs
  set_property -dict { PACKAGE_PIN T14 IOSTANDARD LVCMOS25 } [get_ports { LED[0] }]; #IO_L15P_T2_DQS_13 Sch=led[0]
  set_property -dict { PACKAGE_PIN T15 IOSTANDARD LVCMOS25 } [get_ports { LED[1] }]; #IO_L15N_T2_DQS_13 Sch=led[1]
  set_property -dict { PACKAGE_PIN T16 IOSTANDARD LVCMOS25 } [get_ports { LED[2] }]; #IO_L17P_T2_13 Sch=led[2]
  set_property -dict { PACKAGE_PIN U16 IOSTANDARD LVCMOS25 } [get_ports { LED[3] }]; #IO_L17N_T2_13 Sch=led[3]
  set_property -dict { PACKAGE_PIN V15 IOSTANDARD LVCMOS25 } [get_ports { LED[4] }]; #IO_L14N_T2_SRCC_13 Sch=led[4]
  set_property -dict { PACKAGE_PIN W16 IOSTANDARD LVCMOS25 } [get_ports { LED[5] }]; #IO_L16N_T2_13 Sch=led[5]
  set_property -dict { PACKAGE_PIN W15 IOSTANDARD LVCMOS25 } [get_ports { LED[6] }]; #IO_L16P_T2_13 Sch=led[6]
  set_property -dict { PACKAGE_PIN Y13 IOSTANDARD LVCMOS25 } [get_ports { LED[7] }]; #IO_L5P_T0_13 Sch=led[7]

## Slide 50: MicroBlaze + Custom IP

## Slide 51: Updating Custom IP
Right click on custom IP and click Edit in IP Packager if you want to modify! Otherwise skip to validate design.
1
2
9
9

## Slide 52: Xilinx Vivado – Create and Package Custom IP
Now that you updated the core you need to re-select Review and Package and click the Re-package IP button.

## Slide 53: Updating Custom IP
Refresh IP Catalog, Upgrade IP and then Re-Generate
1
2

## Slide 54: Verify Design
You should verify the addressing for all your design components before continuing.
Verify that the base addresses are the same addresses used in the template C-code.
Should be no changes at this time.
2
3
1

## Slide 55: Validate and Export Design
First click validate design_1
Regenerate the design_1 HDL wrapper.
Finally you need to generate the Generate Design bitstream
Take a coffee break while it builds

## Slide 56: Coffee Break
This Photo by Unknown Author is licensed under CC BY-NC

## Slide 57: Export Design
Exporting Hardware Design to Vitis…be sure to include the bitstream…assuming no errors

## Slide 58: Launch Vitis
Go to Tools, select Launch Vitis IDE, select the .sim folder in your current project folder and click Launch.

## Slide 59: New Vitis Project

## Slide 60: Xilinx Vitis
Click Next

## Slide 61: Xilinx Vitis
Create a new platform…
  Add your previously created XSA file and click next

## Slide 62: Xilinx Vitis
Name project and click next

## Slide 63: Xilinx Vitis
Keep default domain settings and click next.

## Slide 64: Xilinx Vitis
Choose Hello World Application so it creates the platform.c and .h files for the example program.

## Slide 65: Rename helloworld.c
In Vitis' Explorer pane, find the application projects “src” directory. Right click on helloworld.c and rename it to Lec_19.c.

## Slide 66: Xilix Vitis
Copy Lec19.c code from course website.

## Slide 67: Lec19.c

## Slide 68: Lec19.c

## Slide 69: Lec19.c

## Slide 70: Lec19.c

## Slide 71: Lec19.c

## Slide 72: Lec19.c

## Slide 73: Part 2: Software Questions/ Notes related to handout
Why doesn't the 'c' command cause the counter to count up by 1?
On line 130, why did I subtract 0x30?
After loading the counter on line 132, something should be done that is missing.
What line of VHDL code in my_counter_ip_v1_0_S00_AXI.vhd is "activated" when line 80 executes?
What line of VHDL code in my_counter_ip_v1_0_S00_AXI.vhd is "activated" when line 141 executes?
What line of VHDL code in lec19.vhdl "activated" when line 141 executes?
What appears to be the naming convention for hardware registers?

## Slide 74: Add C code to Source File
Copy Lec19.c code from course website.

## Slide 75: Issues with Vitis and IP Cores
Major error with export of Custom IP from Vivado to Vitis. Error may present as:
  Missing xparameters.h error
  Failed to build the bsp sources for domain error
  Cannot find the *.xpfm file
Solutions:
  https://support.xilinx.com/s/article/75527?language=en_US
  https://support.xilinx.com/s/question/0D52E00006jpcvVSAQ/fatal-error-xparametersh-no-such-file-or-directoryxilinx-platform-definition-filexpfm-is-removed-after-building-the-project?language=en_US
  Update both Makefiles in the following Vitis subfolders (otherwise you should be able to update the Makefile in the ip_core driver folder prior to build/export):
    Lecture_19_v.sim\Lecture_19_v_wrapper\hw\drivers\my_counter_ip_vitis_v1_0\src
    Lecture_19_v.sim\Lecture_19_v_wrapper\microblaze_0\standalone_microblaze_0\bsp\microblaze_0\libsrc\my_counter_ip_vitis_v1_0\src

## Slide 76: Issues with Vitis and IP Cores Makefile Solution
  Update the both Makefiles in the following subfolders using the following code (make sure you build the wrapper before the software project):
    Lecture_19_v.sim\Lecture_19_v_wrapper\hw\drivers\my_counter_ip_vitis_v1_0\src
    Lecture_19_v.sim\Lecture_19_v_wrapper\microblaze_0\standalone_microblaze_0\bsp\microblaze_0\libsrc\my_counter_ip_vitis_v1_0\src
COMPILER=
ARCHIVER=
CP=cp
COMPILER_FLAGS=
EXTRA_COMPILER_FLAGS=
LIB=libxil.a
RELEASEDIR=../../../lib
INCLUDEDIR=../../../include
INCLUDES=-I./. -I${INCLUDEDIR}
INCLUDEFILES=*.h
LIBSOURCES=$(wildcard *.c)
OBJECTS = $(addsuffix .o, $(basename $(wildcard *.c)))
ASSEMBLY_OBJECTS = $(addsuffix .o, $(basename $(wildcard *.S)))
libs:
echo "Compiling simple_adder..."
$(COMPILER) $(COMPILER_FLAGS) $(EXTRA_COMPILER_FLAGS) $(INCLUDES) $(LIBSOURCES)
$(ARCHIVER) -r ${RELEASEDIR}/${LIB} ${OBJECTS} ${ASSEMBLY_OBJECTS}
make clean
include:
${CP} $(INCLUDEFILES) $(INCLUDEDIR)
clean:
rm -rf ${OBJECTS} ${ASSEMBLY_OBJECTS}

## Slide 77: Xilinx Software Development Kit - Vitis
In the Vitis environment, you program the hardware built in the previous step.
The key concept here is that the peripheral defined in Vivado design are accessible through the slave registers as memory mapped devices.
Verify your my_counter_ip_v1_0 Base Address in system.hdf file is assigned to be 0x44a00000.
In the my_counter_ip_v1_0_S00_AXI.vhdl file, I (arbitrarily) assigned counter ports to slave register according to the table below.
Signal | direction | Slave Register | Address
D | Input | slv_reg0(7 downto 0) | 0x44a00000
ctrl | Input | slv_reg1(1 downto 0) | 0x44a00004
Q | Output | slv_reg0(7 downto 0) | 0x44a00000

## Slide 78: Xilinx Vitis
Build Application
  To build the project and all of its dependencies, select the system project in the Assistant pane, and either click the Build button ( ), or press Ctrl-B on your keyboard.

## Slide 79: Increase Stack and Heap Size
You may have to add more Stack and Heap to your design
9
9
1
2
3

## Slide 80: Launch Xilinx Vitis on FPGA
Launch a Vitis Baremetal Software Application
  First, many applications require that a serial console is connected to the board, so that standard output (from print statements) can be viewed. For this purpose, a serial terminal like Tera Term. Use a serial terminal application to connect to the board's serial port. Unless otherwise stated, Microblaze designs with an AXI UART Lite IP use a baud rate of 9600.

## Slide 81: Launch Xilinx Vitis on FPGA
Launch a Vitis Baremetal Software Application
  In the Explorer pane at the left side of the screen, right click on the application or system project that is to be run, and select Run as → 1 Launch on Hardware (Single Application Debug). The FPGA will be programmed with the bitstream, the ELF file created by the software build is loaded into system memory, and the application project will begin to run. You will need to click back over to the Vitis Serial Terminal from the Console tab.
You should see the welcome and hitting “?” gives you the menu to observer counter operation on the LEDs

## Slide 82: Re-Exporting Hardware
When you Re-Export Hardware from Vivado to Vitis you have to Update Hardware Specification.

## Slide 83: MicroBlaze + Custom IP