## Slide 1: CSCE 436 - Advanced Embedded Systems Lecture 2 – Digital System, Hierarchical Design, and testbench
Prof Jeffrey Falkinburg Avery Hall 368 472-5120

## Slide 2: Lesson Outline
Time Logs!
HW #1 Due Now!
Overview of HDLs
Basic VHDL concepts by example
Testbenches

## Slide 3: Overview of HDLs

## Slide 4: Programming Language
Can we use C or Java as an HDL?
A computer programming language:
  Semantics ("meaning")
  Syntax ("grammar")
Development of a Language
  Study the characteristics of the underlying processes
  Develop syntactic constructs and their associated semantics to model and express these characteristics

## Slide 5: HDL vs Traditional PL
Traditional PL
  Modeled after a sequential process
  Operations performed in a sequential order
  Help human's thinking process to develop an algorithm step-by-step
  Resemble the operation of a basic computer model
HDL
  Characteristics of digital hardware
    Connections of parts
    Concurrent operations
    Concept of propagation delay and timing
  Characteristics cannot be captured by traditional PLs
  Require new languages: HDL

## Slide 6: HDL vs Traditional PL
HDL continued
  Structural Connections
  Timing
  Parallel Nature

## Slide 7: Modern Use of HDLs
Formal Documentation
Input to a simulator
Input to a synthesizer

## Slide 8: 7400-Series Integrated Circuits
7400-Series Integrated Circuits
  https://en.wikipedia.org/wiki/List_of_7400-series_integrated_circuits
Images from https://www.electronics-tutorials.ws/logic/logic_2.html

## Slide 9: Characteristics of an HDL
Capture characteristics of a digital circuit:
  Entity - basic building block (e.g. 7400 chips)
  Connectivity - Connection of entities (e.g. wires)
  Concurrency - parallel operations
  Timing - schedule / order of multiple operations
Must be able to describe a circuit in
  Gate level and RT level
  Structural view and behavioral view (not physical)

## Slide 10: Highlights of Modern HDLs
Encapsulate the concepts of entity, connectivity, concurrency, and timing
Incorporate propagation delay and timing information
Consist of constructs for structural implementation
Incorporate constructs for behavioral description (sequential execution of traditional PL)
Describe the operations and structures in gate level and RT level
Consist of constructs to support hierarchical design process

## Slide 11: Industry-Standard HDLs
VHDL
  DoD initiative in 1980s
  Transferred to IEEE to standardize
  First released in 1987
  Similar to Ada
  Heavily used in FPGA industry
  New versions: 1993, 2001, 2008
Verilog
  Developed by industry
  Released in early 1980s
  Similar to C
  Heavily used in ASIC industry
  New versions: 1995, 2001, 2005, 2009
  SystemVerilog is a superset of Verilog 2005 & 2009

## Slide 12: Basic VHDL Concepts By Example

## Slide 13: Structural Description
Structural Description from Lesson 1
Truth Table
a b c | f
-------|--
0 0 0 | 0
0 0 1 | 0
0 1 0 | 0
0 1 1 | 1
1 0 0 | 0
1 0 1 | 1
1 1 0 | 1
1 1 1 | 1
Entity
Architecture

## Slide 14: Structural Description
Entity declaration
  i/o ports (“outline” of the circuit)
Architecture body
  Signal declaration
  Each concurrent statement
  Can be thought of as a circuit part
  Contains timing information
  Arch body can be thought as a “collection of parts”
What’s the difference between this and a C program

## Slide 15: Structural Description
In structural view, a circuit is constructed by smaller parts.
Structural description specifies the types of parts and connections.
Essentially a textual description of a schematic
Done by using “component” in VHDL
  First declared (make known)
  Then instantiated (used)

## Slide 16: Structural Description – Component Declaration
library IEEE; -- These lines are similar to a #include in C
use IEEE.std_logic_1164.all;
library unisim; -- Use these libraries if you are using primitive components
use unisim.vcomponents.all;
entity majority is
port( a, b, c: in std_logic;
f: out std_logic);
end majority;
architecture structure of majority is
component AND2
port ( i0, i1 : in std_logic;
o : out std_logic);
end component;
component OR3
port ( i0, i1, i2 : in std_logic;
o : out std_logic);
end component;
signal s1, s2, s3: std_logic; -- wires which begin and end in the component
Component Declarations before Begin
Primitive Components Library

## Slide 17: Structural Description –Component Instantiation
begin
unit1: AND2
port map ( -- s1 <= a and b;
i0 => a,
i1 => b,
o => s1);
unit2: AND2
port map ( -- s2 <= b and c;
i0 => b,
i1 => c,
o => s2);
unit3: AND2
port map ( -- s3 <= a and c;
i0 => a,
i1 => c,
o => s3);
unit4: OR3
port map ( -- f <= s1 or s2 or s3;
i0 => s1,
i1 => s2,
i2 => s3,
o => f);
end structure;
Component Instantiations after Begin

## Slide 18: Behavioral
A behavioral description of a component describes what the circuit does rather than how it is done.
library IEEE; -- These lines are similar to a #include in C
use IEEE.std_logic_1164.all;
entity majority is
port( a, b, c: in std_logic;
f: out std_logic);
end majority;
architecture Behavioral of majority is
begin
f <= '0' when a='0' and b='0' and c='0' else
'0' when a='0' and b='0' and c='1' else
'0' when a='0' and b='1' and c='0' else
'1' when a='0' and b='1' and c='1' else
'0' when a='1' and b='0' and c='0' else
'1' when a='1' and b='0' and c='1' else
'1' when a='1' and b='1' and c='0' else
'1';
-- essentially an enumeration of a truth table
end Behavioral;
Truth Table
a b c | f
-------|--
0 0 0 | 0
0 0 1 | 0
0 1 0 | 0
0 1 1 | 1
1 0 0 | 0
1 0 1 | 1
1 1 0 | 1
1 1 1 | 1

## Slide 19: Behavioral
Concatenation operator helps make code more readable
library IEEE; -- These lines are similar to a #include in C
use IEEE.std_logic_1164.all;
entity majority is
port( a, b, c: in std_logic;
f: out std_logic);
end majority;
architecture Behavioral of majority2 is
signal temp: std_logic_vector(2 downto 0);
begin
temp <= a & b & c;
f <= '0' when temp = "000" else
'0' when temp = "001" else
'0' when temp = "010" else
'1' when temp = "011" else
'0' when temp = "100" else
'1' when temp = "101" else
'1' when temp = "110" else
'1';
end Behavioral;
Concatenation Operator
Double quotes for std_logic_vectors

## Slide 20: Combinational vs Sequential
What is the difference between combinational and sequential?
  A clock signal in the entity for the output

## Slide 21: Literals
In VHDL they are called literals (not a constant)
  hexDigit : std_logic_vector (3 downto 0);
  …hexDigit = x“D” else
  …hexDigit = “0101” else
  …hexDigit = d“12” else
  “=” – used to compare
  “<=” – used to assign
  hexDigit : std_logic_vector (15 downto 0);
  …hexDigit <= x“C0_FF_EE”; --can also use separators

## Slide 22: Testbenches

## Slide 23: Testbench – Component Declaration and Instantiation
ENTITY majority_tb IS
END majority_tb;
ARCHITECTURE behavior OF majority_tb IS
COMPONENT majority
PORT( a : IN std_logic;
b : IN std_logic;
c : IN std_logic;
f : OUT std_logic);
END COMPONENT;
signal s1, s2, s3, s4: std_logic;
begin
uut: majority PORT MAP (
a => s1,
b => s2,
c => s3,
f => s4);
end

## Slide 24: Simple Test Vectors
begin
uut: majority PORT MAP (
a => s1,
b => s2,
c => s3,
f => s4);
s1 <= '0', '1' after 40us;
s2 <= '0', '1' after 20us, '0' after 40us, '1' after 60us;
s3 <= '0', '1' after 10us, '0' after 20us, '1' after 30us , '0' after 40us, '1' after 50us , '0' after 60us, '1' after 70us, ;
end behavior;

## Slide 25: Testbench – Test Vectors for self checking testbenches
Test Vector Setup (before begin):
Loop to apply the 8 test input vectors to majority circuit (after begin)
1. CONSTANT TEST_ELEMENTS:integer:=8;
2. SUBTYPE INPUT is std_logic_vector(2 downto 0);
3. TYPE TEST_INPUT_VECTOR is array (1 to TEST_ELEMENTS) of INPUT;
4. SIGNAL TEST_INPUT: TEST_INPUT_VECTOR := ("000", "001", "010", "011", "100", "101", "110", "111");
1. for i in 1 to TEST_ELEMENTS loop
2. testVector <= test_input(i);
3. wait for 1 us;
4. assert f = test_output(i)
5. report "Error in majority circuit for input " & integer'image(i)
6. severity failure;
7. end loop;

## Slide 26: Testbench – Test Vectors for self checking testbenches
Test Vector Setup:
Loop to apply the 8 test input vectors to majority circuit
1. CONSTANT TEST_ELEMENTS:integer:=8;
2. SUBTYPE INPUT is std_logic_vector(2 downto 0);
3. TYPE TEST_INPUT_VECTOR is array (1 to TEST_ELEMENTS) of INPUT;
4. SIGNAL TEST_INPUT: TEST_INPUT_VECTOR := ("000", "001", "010", "011", "100", "101", "110", "111");
1. for i in 1 to TEST_ELEMENTS loop
2. testVector <= test_input(i);
3. wait for 1 us;
4. assert f = test_output(i)
5. report "Error in majority circuit for input " & integer'image(i)
6. severity failure;
7. end loop;

## Slide 27: Simulation Experimentation
How to add and remove waveforms to the waveform view.
How to change the radix of a vector waveform
How to change the colors of the waveforms.
How to transcend the design hierarchy.
How to observe signal values in design hierarchy.
How to observe signals values in the VHDL code.
How to save a load a simulation waveform wcfg file.

## Slide 28: Even Parity Detection Circuit
Inputs: a(2 downto 0)
Output: even

## Slide 29: Even Parity Detection Circuit
library ieee;
use ieee.std_logic_1164.all;
entity even_detector is
port(
a : in std_logic_vector(2 downto 0);
even : out std_logic
);
end even_detector;
architecture sop_arch of even_detector is
signal p1, p2, p3, p4 : std_logic;
begin
even <= (p1 or p2) or (p3 or p4) after 20 ns;
p1 <= (not a(2)) and (not a(1)) and (not a(0)) after 15 ns;
p2 <= (not a(2)) and a(1) and a(0) after 12 ns;
p3 <= a(2) and (not a(1)) and a(0) after 12 ns;
p4 <= a(2) and a(1) and (not a(0)) after 12 ns;
end sop_arch;

## Slide 30: VHDL Conceptual Diagram

## Slide 31: Alternative Implementation
Same entity declaration
VHDL now contains two architecture bodies (sop_arch is in the "...")
Implicit delta delay

## Slide 32: Lesson Outline
Overview of HDLs
Basic VHDL concepts by example
Testbenches