## Slide 1: CSCE 436 – Advanced Embedded Systems Lecture 20 – Soft Core (MicroBlaze) + Custom IP with Interrupt
Prof Jeffrey Falkinburg Avery Hall 368 472-5120

## Slide 2: Lesson Outline
Time Logs!
MicroBlaze + Custom IP with Interrupt

## Slide 3: Interrupts

## Slide 4: Interrupts
Interrupts are used when you want to your system to do more than one thing at a time.
An interrupt service routine (ISR) is a subroutine called by hardware. The following figure illustrates the process of "calling" and returning from an ISR.

## Slide 5: Interrupts
MCU powers up, jumps to RESET vector
MCU starts execution of main
Dynamic configuration
  configure hardware
  clear hardware interrupt flag
  enable hardware interrupt

## Slide 6: Interrupts
Event occurs which sets interrupt flag
MCU stops running main
MCU saves PC
MCU disables interrupts
Executes "GOTO ISR" at interrupt vector address

## Slide 7: Interrupts
ISR: Poll interrupt flags
ISR: Execute appropriate code in ISR
ISR: Clear interrupt flag
ISR: executes rted
Interrupts are enabled
PC is restored
MCU resumes running main

## Slide 8: Interrupts in the MicroBlaze
Today we will examine how to generate an interrupt into the MicroBlaze.

## Slide 9: MicroBlaze + Custom IP with Interrupt

## Slide 10: MicroBlaze + Custom IP with Interrupt
axi_uartlite_0 @ 40600000
S_AXI_ACLK
S_AXI_ARESETN
slv_reg1
clk
reset_n
ctrl
Artix 7 (design_1)
MicroBlaze
my_counter_ip_v2_0.vhd @ 0x44a00000
my_counter_ip_v2_0_S00_AXI.vhd
Lec20.vhd
32
slv_reg0
Q/D
32
Lec19.xdc
8
LED
T14
T15
T16
U16
V15
W16
W15
Y13
Design_1.xdc
AA19
V18
RX
RX
TX
TX
clk
reset_n
R4
G4
roll
myISR()
main()
slv_reg2
Lec20.c
Interrupt
axi_lite
slv_reg3
flagQ
set
clear

## Slide 11: Lab 3
axi_uartlite_0 @ 40600000
S_AXI_ACLK
S_AXI_ARESETN
slv_reg0  31
To/From Microblaze
clk
reset_n
Lab2 Signals
Artix 7 (design_1 for Lab 3)
MicroBlaze
my_oscope_ip_v2_0.vhd @ 0x44a00000
my_oscope_ip_v2_0_S00_AXI.vhd
Lab2_dp.vhd
32x32
Lab2.xdc
Nets to Pins
Pins off
chip
Design_1.xdc
AA19
V18
RX
RX
TX
TX
clk
reset_n
R4
G4
ready
myISR()
main()
Lab3.c
Interrupt
axi_lite
Signals going In/Out of Artix 7 Chip
Lab2_fsm.vhd
cw
sw

## Slide 12: MicroBlaze + Custom IP – Workflow
The work flow has three main steps.
  Define a new hardware design (MicroBlaze + axi_uartlite) in Vivado IP Integrator (using the MicroBlaze Tutorial from Lecture 18)
  Create and package new custom IP (your custom hardware) and import it into your Vivado design
  Program the resulting hardware in the SDK environment.
Lets start with the first step.

## Slide 13: Xilinx Vivado – IP Integrator
  This step requires that you start a new hardware design (MicroBlaze + axi_uartlite) in Vivado IP Integrator in a new project called Lecture_20.
  You will add a new Block Design with a MicroBlaze and axi_uartlite following the MicroBlaze Tutorial.
https://reference.digilentinc.com/learn/programmable-logic/tutorials/nexys-video-getting-started-with-microblaze/start

## Slide 14: Xilinx Vivado – IP Integrator
  This step requires that you start a new hardware design (MicroBlaze + axi_uartlite) in Vivado IP Integrator in a new project called Lecture_19.
  You will add a new Block Design with a MicroBlaze and axi_uartlite following the MicroBlaze Tutorial.
https://reference.digilentinc.com/learn/programmable-logic/tutorials/nexys-video-getting-started-with-microblaze/start
Don’t Select!

## Slide 15: IP Catalog – Adding IP Repo
Open IP Catalog Settings and click on Repository Manager and add your IP Repo to your IP Repositories
  /path_to_ip_repo/git_repo/ip_repo
1
2
3
4
5
6

## Slide 16: Edit/Create New IP Package
Edit Counter in IP Packager or create a new IP package
I chose to create a new package with a new version.

## Slide 17: Edit/Create New IP Package
Expose the Roll Signal to the Artix 7 (design_1) block diagram by following the LED port maps

## Slide 18: Xilinx Vivado – Create and Package Custom IP
8. Add Custom IP to your design
  8.1) In the project manager page of the original window, click Open Block Design. This adds a block design to the project.
  8.2) Use the Add IP button to add our v2.0 of our Lec 11 Counter IP Core with the exposed roll signal.
Notice it is v2.0

## Slide 19: Edit/Create New IP Package
Click the ‘+’ sign by the MicroBlaze to connect the Roll Signal to the MicroBlaze Interrupt input directly
1
2
3

## Slide 20: Verify Design
You should verify the addressing for all your design components before continuing.
Verify that the base addresses are the same addresses used in the template C-code.
Should be no changes at this time.
2
3
1

## Slide 21: Verify Design
You should verify the addressing for all your design components before continuing.
Verify that the base addresses are the same addresses used in the template C-code.
Should be no changes at this time.

## Slide 22: Validate and Export Design
First click validate design_1
Regenerate the design_1 HDL wrapper.
Finally you need to generate the Generate Design bitstream
Take a coffee break while it builds

## Slide 23: Coffee Break
This Photo by Unknown Author is licensed under CC BY-NC

## Slide 24: SDK Project
Start with a “Hello World” project once in the SDK.
Rename the hello_world.c to Lec20.c and use the given Lec20.c code to get started
Modify the code to handle the interrupt generated from the counter and increment a counter variable for display.

## Slide 25: MicroBlaze Interrupts in C Programming

## Slide 26: MicroBlaze Interrupts
In order to understand how interrupts are handled by the MicroBlaze, its important to understand something about the hardware.
I found most of the following information in the MicroBlaze Users Guide.
  http://www.xilinx.com/support/documentation/sw_manuals/mb_ref_guide.pdf

## Slide 27: MicroBlaze Interrupts
The Machine Status Register contains control and status bits for the processor. Bit 30 of this register, IE, is the interrupt enable.
The MicroBlaze is a three stage pipeline machine - interrupts will need to flush the pipe before proceeding.
The interrupt vector is located at address 0x10-0x14 in memory.
MicroBlaze supports a single interrupt source.
When an interrupt occurs, the following actions happen.
  r14 <- PC
  PC <- 0x00000010
  MSR[IE] <- 0
When the interrupt service routine terminates, control is turned over to the instruction at address r14 and MSR[IE] is set.

## Slide 28: MicroBlaze Interrupts C Programming Example
//-------------------------------------------------------------------------
//-- Name: Prof Jeff Falkinburg
//-------------------------------------------------------------------------
#include <xil_exception.h>
void myISR(void);
int main(void) {
microblaze_register_handler((XInterruptHandler) myISR, (void *) 0);
microblaze_enable_interrupts();
stuff();
} // end main
void myISR(void) {
isrCount = isrCount + 1;
Xil_Out8(countClearReg, 0x01); // Clear the flag and then you MUST
Xil_Out8(countClearReg, 0x00); // allow the flag to be reset later
}

## Slide 29: Manual Easter Egg Hunt
Consult the MicroBlaze Processor Reference Guide and convert the following
  addik r22,r19,1
  swi r23, r1, 60
  bgei r18, -44
Solutions can be found in the source code of the html page

## Slide 30: OS and Libraries Document
Consult the OS and Libraries Document Collection.
  What string formats are supported by the xil_print instruction?