## Slide 1: VET: Autonomous Vehicular Credential Verification using Trajectory and Motion Vectors
Ebuka Oguchi and Nirnimesh Ghose
School of Computing
19th EAI INTERNATIONAL CONFERENCE ON SECURITY AND PRIVACY IN COMMUNICATION NETWORKS
OCTOBER 19 – 21, 2023

## Slide 2: Background
Connected Autonomous Vehicles (CAV) and Unmanned Aerial Vehicles (UAV):
  Avoid Collisions and Hazards ahead
  Platooning
  Safe and efficient traffic control
  Geofencing and Midair colision avoidance, etc.

## Slide 3: Motivation
Traditional Crypto-based veracity verification allows adversaries to inject malicious data by just being in communication range.
Allowing an advanced adversary with powerful antennas can remotely inject data.
Question: How can we securely verify the truthfulness the location and velocity claims
of a vehicle to prevent such attacks?

## Slide 4: Objectives
To develop a framework for credential verification using Trajectory and Motion Vectors (TMVs) for autonomous Vehicles.
B
X
A
M
Prover
Verifier
Verifier x
Adversary
  To build a reliable verification solution that places no assumption on the wireless environment
  e.g, number of reflectors, center frequency etc
  To utilize a location and motion-based authentication strategy to prevent message injection attack
  To perform verification by comparing the claimed TMVs with randomly estimated TMVs

## Slide 5: System Model
The Legitimate Prover A
  A uses omnidirectional antenna
  Has valid credentials (PKI or Symmetric key)
The Verifier B
  Other truthful verifier X
  Perform verification independently
  Verifiers do not require mutual trust.

## Slide 6: Threat Model
  Has valid credentials
  Can additionally intentionally modifying PHY-layer data.
  Has valid credentials
  Within the communication range of B
  Attempting to Inject messages without modifying PHY-layer data
Remote Attacker
Remote Advanced Attacker

## Slide 7: Preliminaries
Frequency of Arrival (FOA) for Velocity Estimation:
2-D or 3-D grid search of provers position
Log-likelihood of the maximum eigenvalues of the Hermitian matrix
Direction Location Estimation:

## Slide 8: VET: Credential Verification using Trajectory and Motion Vectors
Initialization
Transmit Claimed messages
Compute and transmit TMVs to X not to B
A
B
X
Grants Limited Access
Receives , Extract
Captures and Extract
Verification Criterion: ,
Partial access Else Fail
Estimate and Compute tx not to B
Captures extract where
Interpolate with Claimed ,
Verification Criterion:
,
Sniffing packets
Broadcast Decision
Grant Full access Else Fail

## Slide 9: Interpolating TMVs
Cubic Spline Interpolation
  Solving tri-diagonal matrix equation
  Good for complex scenarios ( turn)
  More Accurate, flexible, and smooth.
Interpolation
Cubic spline is better
Location ROC
Velocity ROC

## Slide 10: Formal Analysis of VET: Correctness Analysis
Verification is successful if the Estimated and claimed TMVs
is with the acceptable error .

## Slide 11: Formal Analysis of VET: Robustness Analysis
A Remote Attacker
Two Scenarios
  A is not present, M initiates VET
  A is present, M hijacks the VET

## Slide 12: Security Analysis
  A Remote Advance Attacker
Even for very high probability for TMV 50, 40, 30, 20, and 10. Success probability is very low.
Success Probability
Very low

## Slide 13: Experimental Setup
We utilize a USRP 2922 for the prover A, verifiers B, and X
We broadcast BPSK signals at center frequency running GNU radio code.
The prover and verifiers are connected to a Lenovo ThinkPad T14 laptop
A GPS enabled phone that collects the ground truth location and velocity
All laptops and phone are synchronized to use the same Network time protocol server.

## Slide 14: Experimental Evaluation: Correctness Analysis
We implement FOA and Direct location estimation and compute the ROC
We compare our results with ground truth data.
We evaluate three parameters
    The acceptable errors to set
    The number of trajectory point required to complete the verification
    The acceptable errors for straight and turning trajectory of the vehicle.
ROC for Location
ROC for velocity

## Slide 15: Experimental Evaluation: Robustness Analysis
The Remote Attacker
Velocity
Location
Trajectory
Very low
Very low
VET can detect remote moving adversary attempting to inject rogue messages
As distance increases, the probability of success decreases.

## Slide 16: Experimental Evaluation: Robustness Analysis
A Remote Advanced Attacker
  We compute wireless Channel and
  Adversary utilize the knowledge of the channel to emulate X
  Probability of Success is very low
Velocity
Location
Trajectory
Very low
Very low

## Slide 17: Conclusion and Future Work
We address the problem of secure veracity verification for automomous vehicles
using trajection and motion vectors
We implement a location and motion based strategy that verifies the claimed
TMVs from randomly estimated TMVs
VET can detect remote adversary injecting spoofed messages with 97% true
positives
In the future, we plan to expland our experimental evaluations on UAV platform
with both moving provers and verifiers.
Q&A